Use this section to specify requirements for cast iron medium duty slide gates.  Normally, medium duty slide gates are designed for seating heads up to 6 m and unseating heads up to 3 m, and are fitted with manual operators.  For applications with higher heads, refer to Section 11281 – Heavy Duty Slide Gates.

Carefully co-ordinate this section with Section 05505 – Metal Fabrications if used, particularly where they include similar items.  Close attention to the scope, measurement and payment articles in Section 01280 Measurement Schedule is required, particularly in cases where the metal fabrications specified in this section are being paid for under a Lump Sum, and metal fabrications in Section 05505 – Metal Fabrications are being paid under a Unit Price per kilogram.

Edit this section to suit the Contract requirements.

| Heading of Specification Text | Specification Note |
| --- | --- |
| Part 1 General |  |
| 1.1 References |  |
| 1.2 Submittals |  |
| [.4] | Include this clause for contracts or installations where it is determined that supervision and certification of the gate installation is required. Co-ordinate with clauses 1.3 and 3.1.1. |
| 1.3 [Quality Control] | Include if required, and co-ordinate with clause 1.2.4 and 3.1.1. |
| 1.4 Delivery, Storage, and Handling |  |
| Part 2 Products |  |
| 2.1 Materials |  |
| .2.1 | Review and modify as required to suit design requirements. Review manufacturers gate performance data and material specifications. |
| .3 | Edit stem diameter as required. |
| .4 | Determine the type of manual operator (e.g., geared, handwheel, or square operating nut with T-wrench) required for each installation and edit as required. Normally, the operator is sized such that the gate can be operated with a maximum pull of 111 N (25 lbs). |
| .6 | Edit and include where a thimble is required. Indicate on the Drawings where wall thimbles are required including their lengths. |
| .8.2.1 | SSPC-SP10 provides for a near white metal surface which is normally required for immersion service. Confirm this requirement in conjunction with clause 2.1.8.2.2. |
| .8.2.2 | Intergard 264 is the current paint standard for slide gates being supplied by Armtec. Confirm this in conjunction with clause 2.1.8.2.1. Do not use coal tar epoxy paints which are difficult to repair under moist and cold conditions. |
| Part 3 Execution |  |
| 3.1 Installation and Assembly of Slide Gates |  |
| .1 | Edit in conjunction with clauses 1.2.4 and 1.3. |
| 3.2 Repair of Damaged Coatings |  |

END OF COVER SHEET

PART 1	GENERAL

1.1		REFERENCES

.1	Provide medium duty slide gates in accordance with the following standards (latest revision) except where specified otherwise.

.2	American Society for Testing and Materials (ASTM)

.1	ASTM A36	Specification for Structural Steel.

.2	ASTM A48	Specification for Grey Iron Castings.

.3	ASTM A123	Specification for Zinc (Hot-Dip Galvanized) Coatings on Iron and Steel Products.

.4	ASTM A276	Specification for Stainless and Heat-Resisting Steel Bars and Shapes.

.5	ASTM A307	Specification for Carbon Steel Bolts and Studs.

.6	ASTM A325	Specification for High Strength Bolts for Structural Steel Joints.

.7	ASTM B669	Specification for Zinc Alloys in Ingot Form for Foundry Castings.

.8	ASTM F594	Specification for Stainless Steel Nuts.

.3	American Water Works Association (AWWA)

.1	AWWA C501 	Cast-Iron Sluice Gates.

.4	Canadian General Standards Board (CGSB)

.1	CAN/CGSB 31–GP–3	Corrosion Preventive Compound, Cold Application, Hard Film.

.2	CAN/CGSB-1.181	Ready-Mixed Organic Zinc-Rich Coating.

.5	Canadian Standards Association (CSA)

.1	CSA-G40.21	Structural Quality Steel.

.6	Structural Steel Painting Council (SSPC)

.1	SSPC-SP10	Near White Metal Blast Cleaning.

1.2		SUBMITTALS

.1	Provide the following submittals.

.2	Shop drawings and product data at least 30 days prior to fabrication of the products.  Indicate on the shop drawings dimensions and elevations; materials including specifications; details required to fabricate, locate, and install the slide gates including all related fittings and embedded parts; and coatings including specifications.

.3	Operation and Maintenance Data.

[.4]	The gate manufacturer’s certificate prior to commencing the testing of the slide gates certifying that the installation has been performed according to its recommendations.

1.3		[QUALITY CONTROL]

.1	Provide the services of the slide gate manufacturer’s representative to supervise the installation, testing, and commissioning of the slide gates.

1.4		DELIVERY, STORAGE, AND HANDLING

.1	Inspect each shipment of material and timely replace any damaged materials.

.2	Unload, handle, and store materials in accordance with the manufacturer’s written instructions.  Do not damage the gate or shop-applied coating.  Do not store slide gate components in direct contact with the ground.

PART 2	PRODUCTS

2.1	MATERIALS

.1	Provide slide gates material in accordance with the following.

.2	Medium duty slide gates:

.1	[Armtec Model 20–10C or Waterman C–20] medium duty slide gates with rising gate stems in accordance with AWWA C501 and  having components fabricated from the following materials:

| Component | Material | Specification |
| --- | --- | --- |
| Seat and slide, cross bar, and wedge blocks | Cast iron | ASTM A48, Class 30 |
| Seating face | Aluminum bronze | AWS ECuAl-A1 |
| Structural steel (side, head, and stem support angles) | Galvanized carbon steel | CSA-G40.21–300W, ASTM A123 |
| Stems | Stainless steel | ASTM A276, Type 304 or ASTM A582, Type 303 |
| Fasteners: • bolts • nuts and washers | • Galvanized steel • Stainless steel | • ASTM A307, A325, A123 • ASTM F594, Type 304 |
| Lift and stop nuts | Zinc aluminum alloy | ASTM B669 ZA–12 |
| Adjustable stem guides, with stem collar and bronze bushing, and wall brackets | Cast iron | ASTM A48, Class 30 |
| Pedestals | Galvanized steel | ASTM A36, ASTM A123 |

.3	Gate stems:  Minimum diameter of [28.6] mm.  Stem guides and bronze bushings spaced to limit the slenderness ratio (l/r) of the stem to less than 200.

.4	Manual operator:  [Square operating nut with T-wrench.] [Aluminum handwheel, lift housing, and pedestal] [Geared operator enclosed in a weatherproof cast iron housing equipped with lubrication fittings and mechanical seals, crank, and pedestal.  Incorporate an output shaft extension to permit gate operation using a portable drill unit.]].  Design the operator to permit gate operation with a maximum pull force of [111 N] [177 N].

.5	Stem covers for rising stem operators:  Galvanized steel stem covers fitted with a gate position indicator.

.6	Wall thimbles:  Type [F or E] cast-iron thimbles in accordance with ASTM A48, Class 30.

.7	Hardware:  Screws, bolts, and nuts with threads in accordance with the American National Standards Institute Unified Standard.

.8	Shop coatings consisting of the following:

.1	Machine finished surfaces: Corrosion preventive compound conforming to CAN/CGSB 31–GP–3.

.2	Exposed cast-iron surfaces except for the gear operator housing, prepared, primed, and painted as follows:

.1	Surface preparation:  [Near white metal in accordance with SSPC-SP10].

.2	Finish Coat:  [2 coats, low temperature curing, International Paint Intergard 264 epoxy paint.  Colour: black.]

.3	Manual gear operator housing:  2 finish coats of blue machine exterior enamel paint.

.4	Galvanizing:  Minimum zinc coating of 610 g/m2.

PART 3	EXECUTION

3.1	INSTALLATION AND ASSEMBLY OF SLIDE GATES

.1	Assemble and install the slide gate components in accordance with the manufacturer’s written instructions, at the locations, of the sizes, and at the elevations specified.  [Provide the services of the manufacturer’s representative to supervise the installation, testing, and commissioning of the slide gates.]

.2	Locate and install the wall thimbles and gate frames including anchor bolts in their correct orientation, alignment, and plumb position.

.3	Rigidly support the gate thimble, anchor bolts, and other parts so that they are not displaced during concrete placement.

.4	Place a bead of mastic between the gate frame and the wall thimble to provide a watertight joint.

.5	Accurately align the stem and operator with the gate, and install in a plumb position.

.6	After installation, clean, lubricate, and otherwise service the slide gate components in accordance with the manufacturer’s written instructions.

.7	Test each slide gate by raising and lowering it several times throughout its full range of operation.  Make any required changes or adjustments until the operation of the slide gate is satisfactory to the Minister.

.8	Provide a completed gate installation which has a leakage rate that is below the limits specified in AWWA C501.

3.2	REPAIR OF DAMAGED COATINGS

.1	Prepare damaged paint surfaces and re-coat with paint in accordance with the paint manufacturer’s written instructions.

.2	Repair damaged galvanized surfaces with a zinc-rich paint that is in accordance with CAN/CGSB-1.181.

.3	Power tool clean galvanized surfaces to be repaired to a bright metal surface.  Apply multiple coats of zinc-rich paint in accordance with the manufacturer’s written instructions to obtain a minimum dry film thickness of 50 microns or greater where required by the paint manufacturer.

END OF SECTION