Cargo Securement

On February 1st 2005, Alberta passed legislation that adopted the National Safety Code (NSC) Standard 10, titled Cargo Securement. This standard specifies how a carrier and driver must transport cargo when using a commercial vehicle registered for more than 4,500 kilograms. In general, the standard requires that the cargo must be secured so that it cannot:

- Leak, spill, blow off, fall through, or otherwise be dislodged from the vehicle; or

- Shift upon or within the vehicle to such an extent that the vehicle’s stability or maneuverability is adversely affected.

A copy of the NSC Standard 10 can be obtained through the internet at: http://www.ccmta.ca/english/publicationandreports/publicationandreports.html#cargo.

NSC Standard 10, Cargo Securement, covers both general securement procedures as well as those for specific commodities including: Logs; Dressed Lumber; Metal Coils; Paper Rolls; Concrete Pipe; Intermodal Containers; Vehicles as Cargo; Roll-on/Roll-off and Hook Lift Containers; and Boulders.

This standard contains the minimum requirements that all cargo securement systems must meet. This would include the use of tie downs, anchor points, friction mats, dunnage, etc.

Standard 10 was adopted by the Alberta Cargo Securement Regulation, (AR1/2005). A copy of this regulation can be obtained from the Queen’s Printer.

Commercial vehicles registered in Alberta for less than 4,500 kilograms must secure their cargo so that it meets section 65 of the Vehicle Equipment Regulation (AR322/2002). This regulation is also available from the Queen’s Printer. It is recommended that all commercial carriers and drivers should use the securement criteria outlined in Standard 10 when securing goods, even when operating smaller vehicles.

This information is intended only as a brief introduction to the Regulation and the Standard. Commercial carriers and drivers are strongly encouraged to obtain copies of the Standard and of the Regulation and to ensure that they understand and meet their responsibilities under both.

More Information:

More information on general regulatory compliance may be found in the Traffic Safety Act and regulations that are available through:

Queen’s Printer:		Edmonton:

(780) 427-4952

Web site:   www.qp.gov.ab.ca

Questions on Cargo Securement can be directed to:

Vehicle Safety Section:	Edmonton:

(780) 427-8901

Web site:  www.transportation.alberta.ca

(Toll free in Alberta by first dialing 310-0000)