BASIC RIGHT-OF-WAY REQUEST

For the purpose of purchasing the basic highway right-of-way, the Engineering Consultant will provide right-of-way information on 1:5000 scale digital photo mosaics.  These mosaics are in addition to the mosaics prepared for the functional planning study and are to be constructed to the standards as outlined in Mosaic Production on the previous pages. The mosaics should show clearly and concisely all right-of-way requirements. Prior to submission of the final Right-of-Way Request package, two (2) coloured copies marked “DRAFT” are to be provided to the Property Manager for review and approval.

Once the Right-of-Way Request has been approved by the Property Manager and the Project Sponsor, the Consultant is to provide:

  - Seven (7) sets of colour paper mosaic prints

  - One (1) transparent version with no colour

  - Three (3) coloured mosaics schematic plan showing an overview of the entire project on one sheet. It may be necessary to use two sheets for larger projects. The size of these project overview plans shall not exceed 11”x 17” in size.

  - Individual Ownership Plan’s (IOP’s) showing the proposed right-of-way information for each titled property affected by the project (excepting thereout titled crown land). The IOP shall not exceed 8.5”x14” in size. The contents of the IOP’s shall be consistent with the requirements for the mosaic information required except that only the required right-of-way is to be shaded in red.

  - Plans required by Sustainable Resource Development for the submission of the Provisional Roadway Application on untitled crown lands

  - One (1) electronic copy in .PDF format of all required plans listed above

A thorough and current title search is required on all lands affected by the project. All encumbrances must be reviewed. All encumbrances in the name of Her Majesty the Queen (Minister of Transportation) must be reviewed through the Regional Property Manager for clarification of the nature and extent of the encumbrances/caveats. The date of the title search should be clearly labelled on the mosaics under the title block. In addition, the following information is to be shown clearly on the mosaics:

  - Land ownership, which is to include the landowner’s name and current address, the amount of right-of-way required from each parcel or land affected in both acres and hectares (right-of-way area calculations to be indicated to the nearest 0.1 acres / 0.01 hectares), land title certificate number, legal description, and/or plan number all labelled within the owner’s property. In the case where the parcel of land is too small to record the information within the property boundaries, the information may be shown outside the property with an indicator arrow.

  - Show all Certificate of Title boundaries, surveyed rights-of-way, easements, service road dedications, etc.

  - Any changes or relocation of existing accesses must be shown including alternate means of access (e.g. service road, local road, private drive).

  - Indicate the area of all cut-off parcels or severed land that should be considered for optional purchase by the Department or consolidation with adjacent properties.

  - Show all dimensions of the proposed and existing right-of-way as well as the additional right-of-way requirements, showing the difference between the two.

  - In areas such as subdivisions, towns, etc. where there are properties too numerous to show the required information clearly at the 1:5000 scale, a more detailed plan at a suitable scale may be required. Details on these plans will follow the same requirements as stated in Mosaic Production on the previous pages and this document.

  - In areas through untitled crown lands, the Consultant is to conduct a Land Status Automated System (LSAS) search for all existing land use interests (i.e. Leases, license of occupation, pipelines, etc.) affected by the required right–of-way. The consultant is to obtain any and all plans or sketches that are within the proposed highway right-of-way including ownership of the interests (if available) and record this information on the mosaics to the aforementioned standards.

  - In areas through Special Areas Board land, a Special Areas Board search must be conducted to identify occupants.

  - Identify potential contaminated sites.

  - All mosaic updates and revisions must be consecutively numbered, beginning with Right-of-way request #1.

  - It is required that all right-of-way requirements are to be shown on the mosaic prints highlighted with shading in the appropriate colour to the following format. A colour legend indicating the following must be shown adjacent to the title block, on each mosaic sheet.

  - Right-of-way required	RED

  - Previously requested right-of-way	GREEN

  - Cancellation of previously requested right-of-way	YELLOW

  - Requested easements	ORANGE

  - Optional purchases	CROSSHATCHED (RED)

  - Possible borrow locations	10cm diam. RED CIRCLE

  - Each mosaic sheet title block must indicate “Preliminary Design”, the date of mosaic preparation, and “Right-of-Way Request Number”.

| Required information | Sample of preferred format |
| --- | --- |
| Legal Description C. of T. number Landowner name/s Landowners address R/W required (Provide separate areas for highway r/w and Service road r/w) (Red) Previously requested r/w (Green) Cancellation of previously requested r/w (Yellow) Requested Easement (Orange) Optional purchase (Cross Hatched Red) Possible borrow locations (Red Circle 10 cm dia.) | NE 27-73-4-W6M or Plan /Block/Lot 962 305 963 Bob Smith and Cathy Smith Box 1234, Worsley, AB T0H 3P0 Required Highway R/W - 5.9 ac (2.38 ha) Required Service Road R/W - ac ( ha) Previously requested R/W – 5.2 ac (2.10 ha) Cancelled R/W – 2.5 ac (1.01 ha) Easement – 1.3 ac (0.5 ha) Optional purchase / cut-off –29.6ac (11.98 ha) Total R/W required - ac ( ha) Possible borrow location – 10 cm diam. Red circle Note: Use only the headings that are applicable. |
| Information to be indicated in the upper right corner (Title Block) A Right-of-Way request form is required for each revision to the r/w requirements | Right-of-way Request # 3 - June 21, 1999 Preliminary Design, For Discussion Purposes Only |