| ALBERTA Transportation Technical Standards Branch | Date: Aug 31, 2011 |
| --- | --- |
| SURFACING ESTIMATE WORKSHEET | File: Hwy. 41:08 |
| Designed by: D.C. | Hwy. 545:02 |
| Reviewed by: M.J. | A.R. 154 |
|  | BID ITEM SUMMARY |  |
| DESCRIPTION | Hwy. 41:08 | Hwy. 545:02 | A.R. 154 | TOTAL | UNITS |
| Mobilization | $269,356 | $91,039 | $38,434 | $398,829 | Lump Sum $ |
| Supply of Aggregate - With Option | 39,200 | 13,000 | 5,400 | 57,600 | t |
| Subgrade Excavation | 400 | 100 |  | 500 | m3 |
| Granular Fill (Pit-Run) Des. 6 - 125 | 500 | 150 |  | 650 | t |
| Granular Fill Des. 2 - 25 | 500 | 150 |  | 650 | t |
| Asphalt Concrete Pavement - E.P.S. Mix Type L1/200-300A |  | 12,700 | 5,400 | 18,100 | t |
| Asphalt Concrete Pavement - E.P.S. Mix Type M1/200-300A | 24,900 |  |  | 24,900 | t |
| Asphalt Concrete Pavement - E.P.S. Mix Type S1/200-300A | 13,300 |  |  | 13,300 | t |
| Roadway Lines - Supplying Paint & Painting Directional Dividing + 2 Edge | 17.38 | 6.51 | 5.09 | 28.98 | km |
| Roadway Lines - Supplying Paint & Painting Lane Dividing Lines - Turnout | 0.32 |  |  | 0.32 | km |
| Intersection Lines - Supplying Paint & Painting All Lines | 1 |  |  | 1 | unit |
| MATERIAL SUMMARY |
| DESCRIPTION | Hwy. 41:08 | Hwy. 545:02 | A.R. 154 | TOTAL | UNITS |
| UNIT PRICE TO BE PROVIDED BY THE REGIONAL AGGREGATE COORDINATOR FOR ALL OPTION |
| SOURCES AND TO BE INSERTED INTO THE UNIT PRICE SCHEDULE BY THE PRIME CONSULTANT |
| i.e. 57,600t @ $2.50/t = $144,000 |

| ALBERTA Transportation Technical Standards Branch | Date: Aug 31, 2011 |
| --- | --- |
| SURFACING ESTIMATE WORKSHEET | File: Hwy. 41:08 |
| Designed by: D.C. | Hwy. 545:02 |
| Reviewed by: M.J. | A.R. 154 |
|  | COST SUMMARY |  |
| DESCRIPTION | Hwy. 41:08 | Hwy. 545:02 | A.R. 154 | TOTAL |
| Mobilization | $269,356 | $91,039 | $38,434 | $398,829 |
| Supply of Aggregate - With Option | $98,000 | $32,500 | $13,500 | $144,000 |
| Subgrade Excavation | $6,720 | $1,680 |  | $8,400 |
| Granular Fill (Pit-Run) Des. 6 - 125 | $10,000 | $3,000 |  | $13,000 |
| Granular Fill Des. 2 - 25 | $16,500 | $4,950 |  | $21,450 |
| Asphalt Concrete Pavement - E.P.S. Mix Type L1/200-300A |  | $863,600 | $367,200 | $1,230,800 |
| Asphalt Concrete Pavement - E.P.S. Mix Type M1/200-300A | $1,618,500 |  |  | $1,618,500 |
| Asphalt Concrete Pavement - E.P.S. Mix Type S1/200-300A | $931,000 |  |  | $931,000 |
| Roadway Lines - Supplying Paint & Painting Directional Dividing + 2 Edge | $12,427 | $4,655 | $3,640 | $20,722 |
| Roadway Lines - Supplying Paint & Painting Lane Dividing Lines - Turnout | $161 |  |  | $161 |
| Intersection Lines - Supplying Paint & Painting All Lines | $251 |  |  | $251 |
| SUB-TOTAL | $2,962,915 | $1,001,424 | $422,774 | $4,387,113 |
| CONSTRUCTION COST (rounded) | $2,963,000 | $1,002,000 | $423,000 | $4,388,000 |
| CONTINGENCY (5%) | $148,150 | $50,100 | $21,150 | $219,400 |
| ENGINEERING (10%) | $311,115 | $105,210 | $44,415 | $460,740 |
| TOTAL ESTIMATED COST (rounded) | $3,422,000 | $1,157,000 | $489,000 | $5,068,000 |

| ALBERTA Transportation Technical Standards Branch | SURFACING ESTIMATE SUMMARY |
| --- | --- |
| Project: | Hwy. 41:08 | From km: | 21.850 | To km: | 39.229 |  |
| Project: | Hwy. 545:02 | From km: | 0.000 | To km: | 6.511 |  |
| Project: | A.R. 154 | From km: | 0.000 | To km: | 5.124 |  |
| PMB | Bid Item | Unit | Estimated | Unit | Estimated | Spec | Remarks |
| Code # | Decription |  | Quantity | Price | Cost | Nos. | (Plan No.) |
| X100 | Mobilization | Lump | 1 | Lump | $398,829 | 1.2 |  |
| A800 | Supply of Aggregrate – With Option | t | 57,600 | $2.50 | $144,000 | 3.2 & S.P. |  |
| B100 | Subgrade Excavation | m3 | 500 | $16.80 | $8,400 | 3.1 |  |
| B152 | Granular Fill (Pit-Run) Des. 6 - 125 | t | 650 | $20.00 | $13,000 | 3.8 |  |
| B153 | Granular Fill Des. 2 - 25 | t | 650 | $33.00 | $21,450 | 3.8 |  |
| Q992 | Asphalt Concrete Pavement - EPS (Mix Type M1/200-300A) | t | 24,900 | $65.00 | $1,618,500 | 3.50 |  |
| Q993 | Asphalt Concrete Pavement - EPS (Mix Type L1/200-300A) | t | 18,100 | $68.00 | $1,230,800 | 3.50 |  |
| Q994 | Asphalt Concrete Pavement - EPS (Mix Type S1/200-300A) | t | 13,300 | $70.00 | $931,000 | 3.50 |  |
| S350 | Roadway Lines – Directional and 2 Edge Lines | km | 28.98 | $715.00 | $20,722 | 7.2 |  |
| S355 | Roadway Lines - Lane Dividing Line - Turnout | km | 0.32 | $501.00 | $161 | 7.2 |  |
| S360 | Roadway Lines – Intersection Lines | Unit | 1 | $251.00 | $251 | 7.2 | Int. 381 |
|  | Total | $4,387,113 |  |
|  | Total Estimated Contract Cost (rounded) | $4,388,000 |  |
|  | Contingencies @ 5% | $219,400 |  |
|  | Total Estimated Contract Cost + Contingencies | $4,607,400 |  |
|  | Engineering @ 10% | $460,740 |  |
|  | Total Estimated Cost (rounded) | $5,068,000 |  |
|  | Prepared By: R.G. | Date: Aug/31/11 |
|  | Checked By: M.J. | Date: Aug/31/11 |