## Slide 1: APPROACH ROAD INSPECTION AND RATING

## Slide 2: Introduction
Approach road is the road leading up to the bridge or culvert
Basic rule is alignment OVER is rated in Approach Road section and Alignment UNDER is rated in Grade Separation or Channel section
For purpose of this presentation – not road under bridge or through culvert – covered in GS
For culverts it includes the road fill over the culvert
Considerations for rating
  Geometric alignment at the bridge site
  Condition of approach fill
  Inventory and condition of guardrails on approaches
  Drainage on approaches to bridge

## Slide 3: Road Use
Roads are used by:
People with reduced abilities
People who just got licensed or new to driving
Inattentive drivers
Dangerous / erratic drivers
Drivers unfamiliar with the area
Vehicles/Tires in poor condition
All of these factors have to be accommodated by the approach road alignment.

## Slide 4: Approach Road Section - Bridges

## Slide 5: Approach Road Section - Culverts
Upstream End
Direction
Wingwalls
(Shape : )
End Treatment (Concrete,
Steel, Others, None)
Collar/Concrete Slope Protection
Headwall

## Slide 6: Alignment
Separate ratings are provided for horizontal and vertical alignments
Defects in alignment must be categorized in either the horizontal or vertical components
Inspector should consider road alignments are used during adverse weather or road conditions – e.g. fog, heavy rain, snow, un-gravelled surfaces, icy roads

## Slide 7: Length of Approach

## Slide 8: Length of Approach

## Slide 9: Alignment
Design speed is the posted legal speed for road plus 10 kph
Evaluate by driving legal speed limit - if safe to do so and conditions permit.
Observe sight distances
Note if bridge is super-elevated
Note presence of speed limit or other signs
  Sharp curve
  Steep hill
  Intersection ahead
    Could indicate sight distance problem

## Slide 10
Horizontal defects result in a reduction in speed to drive the road safely. They include:
  Reduced visibility – trees, buildings, embankments
  Sharp corners
  Intersecting or access roads
  Bridge is at beginning of or in curve
  Bridge is offset from straight alignment
  Limited sight distance for passing safely
Horizontal Alignment

## Slide 11: Horizontal Alignment Ratings
Note presence and record location of intersections or access roads including residential or commercial (field accesses do not affect rating).
  Rate 7 or less depending on visibility, traffic volume and traffic type.
  Rating may be 8 or 9 if on tangent and no intersections within 1km
If horizontal defect is cause of reduced speed, then rate:
  6 or more if driven safely at legal speed limit
  5 can be driven safely and posted not more than 20 km/hr below legal speed limit
  4 or less if posted more than 20 km/hr below the legal speed limit
  4 or less if sharp or blind curves
  5 if Land Access bridge and appropriate warning signs are in place
Rate 2 if combined effect of horizontal and vertical alignment is hazardous (e.g. very steep hill combined with sharp hair-pin curve)

## Slide 17
Vertical alignment defects result in a reduction in speed to drive the road safely. They include:
  Reduced visibility – crests
  Steep grades (take into consideration road surface e.g. loose gravel)
  Adequate sight distance for stopping or passing
  Intersecting roads
Vertical Alignment

## Slide 18: Vertical Alignment Rating
Vertical alignment with a straight grade of 1% or less - rate 9
If road can be driven safely at legal speed limit rate 6 or more
If road can be safely driven and posted not more than 20 km/hr below legal rate 5
Rate 4 or less if:
  posted more than 20 km/hr below posted speed
  sight distance is less than required
  Steep grades, blind crest curves
Rate 2 if combined effect of horizontal and vertical alignment is hazardous (e.g. very steep hill combined with sharp hair-pin curve)
Rate 5 if Land Access bridge

## Slide 22: Alignment – Vertical And Horizontal
For land access structures:
  Road services land only, not residential access, minimal traffic
  Appropriate warning signs in place
  Previous rating guidelines do not apply – rate 5
Alignment of railway, pedestrian and animal overpasses, and utility structures crossing over top are rated X
If both Horizontal and Vertical alignments rated X, General Rating is rated 5.
  Pedestrian bridges over streams/watercourse or roadways
  Grade Separation - Wildlife crossing over top of roadway
  Grade Separation - Railway crossing over roadway

## Slide 23: Culvert Grade Separation – Wildlife Over Horizontal & Vertical Approach Road Alignment Rated X so Gen. Rating = 5

## Slide 24: Culvert Grade Separation - Wildlife Overpass Vertical & Horizontal Road Alignment OVER Rated X, Gen. Rating = 5

## Slide 25: Pedestrian Bridge – Stream Under Horizontal & Vertical Approach Road Alignment Rated X – Gen. Rating =5

## Slide 27: Roadway Width
This is the width of the traveled lanes and shoulders
Do not include median width if present on approach road
If curbs on the approach road, measure between faces
Measure at a representative cross-section
Record minimum width to the nearest 0.1m if different between ends
Provide explanation if different on each side of structure

## Slide 28: Roadway Width

## Slide 29: Approach Bump
Bridges only
Refers to the smoothness of the transition onto the structure
Severe bump
  Can be hazard to traffic (2 or less)
  Can lead to increased impact loading on structure (4 or maybe 3 or less)

## Slide 30: Approach Bump
May be a symptom of
  Settlement of the approach fill
  Instability of the fill (slumping)
  Undermining of fill by water
  Settlement of or damage to approach slab
Drive over at legal speed if safe – or at safest speed that conditions allow
Observe traffic crossing structure
If no defects and smooth transition rate 9
If bump is noticeable but tolerable - rate 5
If speed must be reduced - rate 4 or less
If causing significant impact loading on bridge deck – rate 3 or less
If hazardous to traffic - rate 2 or less

## Slide 31: Guardrail
Refers to guardrail or other traffic barrier along edges of the approach road
Purpose:
  Prevent traffic from leaving the roadway at the structure
  Prevent traffic from impacting structure

## Slide 32: Guardrail - Culverts
Rating is not required
Record the presence of guardrail by Yes or No
Provide comment if guardrail is on one shoulder only
Guardrail that is too short or is otherwise ineffective – provide comment and maintenance recommendation
Provide comment and maintenance recommendation if missing and is required for safety
Note defects (e.g. - broken posts, damaged rails) and provide comment and maintenance recommendation
No indicates no guardrail

## Slide 33: Guardrails - Bridges
Record the presence of guardrail by Yes or No
Record the minimum length to the nearest meter
  Comment/Explain if different lengths exist
Maximum is 99 m
Record the type of termination
  Common type is Turned Down End, Wing End, Attenuator, Fleat
Built based on current Standard Drawings
Since 2001 most common S1643, 1649, 1651, 1652, 1653, and S1705 (newest)
Record if the guardrail meets current standards (Yes/No)
  Explain if “No”
  Common acceptable explanation is “Not thriebeam” or “Not attenuator”
HTCB is currently preferred standard and may transition with W-beam
https://www.alberta.ca/assets/documents/trans-bridge-barrier-drawings.pdf

## Slide 34: Guardrails - Bridges
Inspect up to 20 m from bridge
Inspect all components of guardrail
  Posts
  Rail or Cable if HTCB
  Connections
  Splices
  Termination (if within 20 m). Comment is more than one type
Rate according to condition only - not standard
  e.g. do not down-rate if not built to current standard. Rate condition and functionality
  E.g. W-beam 550mm road top to center – down-rate if too low or high to function

## Slide 35: Guardrails - Bridges
Inspect up to 20 m from bridge
Inspect all components of guardrail
  Posts
  Rail
  Connections
  Splices
  Termination (if within 20 m)
Rate according to condition only - not standard
Minor damage but still functional – rate 5
Missing bolts or improper laps - 4 or less
Damaged - requires replacement – rate 3 or less
Damaged – potential hazard – rate 2 or less
Rate “X” if no guardrail exists
  If required, comment and recommendation

## Slide 36
New W-Beam guardrail installed with Fleat 350 Energy Absorbing Terminals
By design, the 3rd post from the Fleat 350 Terminal is left unbolted from the rail. Does not affect the guardrail rating.
Guardrails – RDG-B1.5

## Slide 37
http://www.transportation.alberta.ca/Content/docType233/Production/RDG-B1-5.pdf

## Slide 47: Drainage
Applies to bridges only
Refers to the ability of the approaches to handle drainage
  Must not allow water to drain onto structure
  Must not allow damage to fills or headslopes
  Must not pond on approaches
Includes drain troughs on approaches
Water may originate from
  Precipitation onto approaches
  Runoff from roadway
  Runoff from structure

## Slide 48: Drainage
Look for:
  Ponding of water on approaches or ends of structure
  Erosion of fills, road embankment, headslope or ditches
  Voids under approach slabs or abutments
  Undermining of drain troughs
  Damage or deterioration of drain troughs

## Slide 49: Drainage
Good drainage away from bridge – rate 5 or more
Drainage onto bridge gutters - rate 4 or less
Drainage onto bridge driving lanes-rate 3 or less
Drainage eroding headslope or sideslope – rate
4 or less
Erosion from approach road ditch drainage – rate 4 or less
Drainage causing a hazard - rate 2 or less (e.g. ponding or icing into travel lanes)

## Slide 55: Embankment
Applies to culverts only
Rates the stability of the road embankment at the culvert and the effects on:
  traffic
  structural and functional integrity of the culvert
Evaluates:
  roadway surface
  Side slopes
  transitions at ends of culvert

## Slide 56: Embankment – Culvert Approach Road

## Slide 57: Embankment
Refers to Culvert Approach Roads
Look for:
  cracks or other evidence of instability
  signs of erosion such as gullying on sideslopes
  scour at toes of sideslopes or end transitions
Embankments with no instability or scour/erosion - rate 7 or better
Embankments with erosion problems - rate 4 or less
Unstable embankments causing damage to the culvert - rate 3 or less
Unstable embankments affecting roadway - rate 3 or less

## Slide 58: Sideslopes
Not rated
Estimate or measure the slope of the sideslope (h:v)
Record steeper of upstream or downstream sideslope
If berms or different slopes on the same side, record steepest slope
  Do not record average slope
Explain if sideslopes are irregular
  varying slopes
  benches or berms
  different slopes on each sideslope

## Slide 59: Sideslopes

## Slide 61: Height of Cover
Inventory item (grey box on form). Record if blank, revise if incorrect.
The vertical distance between top of roadway at centerline and top of the culvert at the upstream end
Need to be accurate, especially for low covers
  Live load effects are greater
Record to the nearest 0.1m

## Slide 62: Height of Cover
Top of Road
Top of Roof at U/S
Flow

## Slide 64: General Rating
Refer to 1.10. 1 and 6.8 (Bridges)
Refer to 1.10.6 and 13.4.6 (Culverts)
Governing Elements
  Horizontal alignment
  Vertical alignment
  Safety Concerns (severe approach bump)
  Potential hazards (Drainage causing ponding/icing
  Embankment rating of 3 or less (Culverts)
  Guardrail that is damaged resulting in a hazard (i.e. missing sections)
No approach rails but hazardous governs the General Rating (rate 2)
Horizontal and Vertical alignment rated X – General rating is 5

## Slide 65: Questions?