## Slide 1
Hydrotechnical Design and Fish Passage Considerations
AT-DFO Committee
July 2022

## Slide 2
Hydrotechnical Design Basics
Culvert Sizing
Fish Passage
Overview

## Slide 3
Component | Governs | % System
Channel Capacity | Most channels | > 80%
Historic Highwater | Large streams | ~ 10%
Runoff Potential | Small basins | < 5%
Hydrotechnical Design
*since ~2001
Notes: HDG:
Established in 2001
3 components
Examples provided for > 1500 bridge sites in HIS
Historic HWM seldom >> Qcc, usually confirms
Runoff Potential – seldom governs, important when it does

## Slide 4
Channel Capacity
Notes: Physics:
Most channels have trapezoidal shape up to bankfull
Beyond this level, much of water goes into storage
Does runoff make the channel or does channel control the runoff? - Yes

## Slide 5
Channel Capacity
Notes: Typical Rating Curve:
Qcc >> Qh
Increase in A and V due to increase in Y

## Slide 6
Historic Highwater
*HIS database on GOA website
Notes: AT Records:
Access in HIS
Flood records and file histories
> 4000 event-site combinations – flood records
Photos, measurements
Look u/s and d/s for more coverage

## Slide 7
Basin Runoff Potential
~3000 events analyzed across Province
Qbrp = unit runoff rate X drainage area
Notes: Basin Runoff Potential
Upper bound check – ability of basin to supply water if routing was not a constraint
Analysis of >3000 runoff events at WSC gauges
Geographic assignment based on envelope curves for distinct hydrologic districts
Map created for design use

## Slide 8
~1500 in HIS
Hydrotechnical Summary
Notes: Putting it all together:
Hydrotechnical summaries published for >1500 bridges (most of the big ones)
Combine 3 components to one set of parameters

## Slide 9
Other Considerations
Notes: Don’t be too precise:
Drift
Ice
Alignment changes
Channel changes

## Slide 10
Channel Hydraulics

## Slide 11
S
1
Y
V = 14 Y0.67 S0.4
Natural Channel Flow
Q = VA
Water surface
Streambed
Notes: Water surface is parallel to the streambed; velocity related to

## Slide 12
Undersized
Right Sized
Flow = Velocity *Area
If area ; velocity
Oversized
Notes: Relationship between V and A; issues with too small and too big
Goal to have structure similar to natural channel
Need to do hydraulic calculations to evaluate sizing options

## Slide 13
Velocity lines: tighter = faster
ROAD
EMBANKMENT
CULVERT
Notes: Exaggerated view of constricted opening in plan view:
Contraction of flow u/s – relatively efficient.
High velocity through culvert.
Expansion of flow d/s, less efficient, eddies.

## Slide 14
S
1
Normal
Rapidly varied flow
Gradually varied flow
Undersized and perched culvert
Historically…
Water surface
Streambed
Culvert

## Slide 15
Notes: Inlet – relatively smooth transition

## Slide 16
Notes: Outlet – rough transition

## Slide 17
D/S Channel
Transition
Current Practice
*Design Flow conditions
Freeboard
Notes: D/s Channel – often normal flow : Sf = So (balance gravity with resistance)
D/S Transition – Adverse flow profile due to burial
Outlet – RVF due to expansion of flow (headloss over short distance, different shape of flow, ~ V2)
Barrel – usually GVF due to BW from burial, may approach normal flow, may have jump, may be full or partial full flow
Inlet – RVF due to contraction of flow (change in shape, less headloss than expansion)
U/S Transition – steep slope due to burial but rough due to rock, too short to form predictable profile
U/S Channel – usually GVF (due to accumulated headloss), approaching normal flow some distance u/s (length varies inversely with slope)

## Slide 18
Overview Hydraulic Sizing:
Complex hydraulics – need modelling
Comparable to natural channel
Other parameters - road design, geotechnical, drift, ice, future needs, wildlife, fish passage*)
Consider options, assess pros/cons/risks
*Bridge Conceptual Design Guidelines

## Slide 19
Fish Passage

## Slide 20: Fish Passage - A Brief History
3Q10
  Wait 3 days, ok to not pass 1/10 years
  First used in 1979, Alaska study w/ Artic Grayling
  1:10 year first noted in 1992 at GOA
  Stats and flow data needed
    30+ years to get 10 year flow
Every species, every stream?
Fish impacts?
Notes: Fish Habitat Protection Guidelines (1992, AESRD)
Why ten years, impact on fish species?
Artic grayling vs bull trout

## Slide 21: A Brief History
Fish Swimming Database & Performance Curves (Katapodis, DFO 2016)
  “Most data from .. swim tunnels”
  Average velocity
  Fish motivation?
Notes: 2000 sources – English language; US, Canada, others
Tunnel vs culvert velocity
Swimming because being forced to vs needing food/spawning
Running on treadmill vs on a soccer field vs being chased by a bear

## Slide 22: A Brief History
  collapsing data, trend lines
  “average values rather than measurements from individual fish”
  131 species grouped into 6 categories
Notes: Impact of grouping data
What if data was wrong?
75% interval lines more spread out
Single data point to create a line

## Slide 23
Is there a better way?
Physical channel parameters vs extrapolated math?
Apply to all fish and all streams?
Alberta’s Approach
Notes: Physical approach, could work across all sites and species?
41 gauges of about 1100 in province

## Slide 24
In 2007
  Study with DFO
  WSC Gauges with 30+ years, DA’s <100sqkm
  3Q10 flow calculated for each gauge
  Flow, depth, velocity calculated at 3Q10 flow
Alberta’s Approach

## Slide 25
Y vs S relationship
Alberta 2008 Method
  Assess range of Y
  Vculvert < Vchannel
Alberta’s Approach

## Slide 26: Alberta’s Approach
2012 Study Update
  Specific period of the year
  DFO: Mar 1 - May 15, Sept 1 – Oct 30
Calculated Y,V,Q values for 3Q10
Notes: 2012
We know fish are more likely to move at certain times of the year such as spring spawning

## Slide 27
Compared Qmax vs 3Q10
3Q10 (98.7%) - under flood conditions (red)
Q > normal, Q < flood? (yellow)
Average flow (green)
Alberta’s Approach
Chart: % Time Flow Exceeded
| 0 | 5 | 10 | 15 | 20 | 25 | 30 | 35 | 40 | 45 | 50 | 55 | 60 | 65 | 70 | 75 | 80 | 85 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100
Q / 3Q10 | 0.0034989 | 0.0086343 | 0.01148 | 0.014468 | 0.017747 | 0.020863 | 0.024244 | 0.028274 | 0.032847 | 0.038716 | 0.04535 | 0.05358 | 0.064258 | 0.077136 | 0.094534 | 0.11793 | 0.14985 | 0.20003 | 0.29542 | 0.32286 | 0.35955 | 0.39826 | 0.44876 | 0.50459 | 0.57297 | 0.66956 | 0.84807 | 1.2081 | 3.9977
 | 0 | 1
Notes: Evaluate at Q > normal, Q < flood
Choose Qfpd – only exceeded 5% of days
Calculate hydraulically (no statistics)
1990 flood

## Slide 28: Alberta’s Approach
Evaluated Y @ Q98, Q95, Q90
Envelope curves
Yfpdd = 0.8 – 34.3*S
Notes: DFO conversation. They suggested Q95

## Slide 29: Alberta’s Approach
Vculv < Vchannel @ Qfpdd
Culvert Embedment (D/4)
Stream simulation approach
Notes: Sediment transfer

## Slide 30: Alberta’s Approach
Backwater – Y up, V down
Backwater from burial
Prevent hanging outlet
Sediment processes

## Slide 31
Velocity Reduction Options – NOT Effective
Increase Pipe Diameter - mostly air space
Increase Burial – ineffective >1m, ponding, u/s barrier, excavation?

## Slide 32
Velocity Reduction Options - Effective
Increase Roughness – substrate holders
Multiple Pipes – wide, shallow channels; consider drift blockage
Shape (Box, Ellipse) – cost, hydraulics?
If none work - bridge

## Slide 33: Substrate Holders
Beneath Streambed
Holds substrate for stream simulation
Increased Roughness
vs baffles
sediment accumulation
easily damaged

## Slide 34: Substrate Holders
Design Guidelines for Bridge Sized Culverts
the following parameters are recommended:
• Substrate holder should be made of steel and conform to the shape of the pipe up to the desired height.
• Height of substrate holder should be 0.3m (0.2m if pipe diameter < 3m)
• Spacing of holders should be in the range of height divided by slope of pipe (minimum spacing = 7m)
• Substrate should be Class 1M or Class 1 rock, with an average thickness matching the height of the holder.
• Substrate and holders are only required where the mean velocity exceeds the mean channel velocity (typically the upstream portion of the pipe).

## Slide 36
QUESTIONS?
Microsoft Word - Fish Passage Design Summary.docx (alberta.ca)