## Slide 1
STANDARD BRIDGE & CULVERT COMPONENTS

## Slide 2: Alberta Bridge Inventory
In Alberta there are about 13,300 bridges.
Types of bridges in Alberta:
  Standard bridges 3521 (26%)
  Bridge size culverts 8348 (63%)
  Major bridges 1435 (11%)

## Slide 3: Standard Bridges
-Any bridge which is built using standard components and according to standard drawings (plans).
-Exception is standard girder bridges with composite decks (e.g. – SMC, SCC, SLC) which are currently classified as major bridges
-For inspection purposes standard bridges are divided into two basic features:
  Superstructure
  Substructure

## Slide 4: Typical Bridge Components
DECK
SUPERSTRUCTURE
PIER PART OF
SUBSTRUCTURE
ABUTMENT PART OF
SUBSTRUCTURE

## Slide 5: Typical Bridge Components
Superstructure
  It carries the load applied to the deck and transfers it to bridge supports.
Substructure
  It transfers load from the superstructure to the foundation soil or rock.
  It includes all elements below the bearings.

## Slide 6: Typical Bridge Components
Deck
- Provides a smooth & safe riding surface
  Transfers load of the deck to other components.
  Three common material used for the deck:
      Wood
      Concrete
      Steel

## Slide 7: Superstructure for Standard Bridges
Superstructure comprises of bearings and all elements above bearings, including:
  Bridgerail.
  Hazard markers.
  Timber stringers with timber deck.
  Reinforced concrete girders.
  Prestressed concrete girders.
  Bearings.

## Slide 8: Superstructure Elements
SUB DECK AND STRINGERS ARE
TREATED WITH CREOSOTE.
NOTE:
SPLICE - EXPOSED EDGE
FACES AWAY FROM
APPROACHING TRAFFIC
TIMBER POST
W - BEAM BRIDGERAIL
WHEEL GUARD
STRIP DECK
SUB DECK
TIMBER STRINGERS
TIMBER BLOCK
AT EVERY POST
Timber
Superstructure

## Slide 9
Superstructure
S
u
b
structure
APPROACH
GUARDRAIL
W BEAM
BRIDGERAIL
HAZARD MARKER
CONCRETE CAP
STEEL PIPE PILE
STEEL H - PILE
CURB
CONCRETE
GIRDER
NEOPRENE
BEARING PAD
S
uperstructure
S
u
b
structure
TUBE TYPE
BRIDGERAIL
HAZARD MARKER
CURB
CONCRETE
GIRDER
TIMBER CAP
TIMBER PILE
SPAN 1
SPAN 2
SPAN 1
SPAN 2
Superstructure Elements

## Slide 10
APPROACH RAIL TRANSITION
3.4 mm THICK
THRIE BEAM GUARDRAIL
CONCRETE CAP
STEEL PIPE PILE
STEEL H - PILE
CONCRETE
GIRDER
NEOPRENE
BEARING PAD
SPAN 1
SPAN 2
BRIDGERAIL
GUARDRAIL
3.4 mm THICK
THRIE BEAM GUARDRAIL
2.7 mm THICK W-THRIE BEAM
TRANSITION SECTION
TOP OF FINISHED ROADWAY
Superstructure Elements

## Slide 11
Reinforced Concrete Girders
  Concrete is strong in compression and weak in tension.
  Concrete bending members are reinforced with mild reinforcing steel to produce reinforced concrete girders.
Prestressed Concrete Girders
  Girders are reinforced with high strength steel under tension.
  Girders are designed not to crack.
  Generally more economical.
Superstructure Elements

## Slide 12
Reinforced Concrete
Girders
Superstructure Elements
TYPE "A" INT.
TYPE "A" CURB
TYPE "G" INT.
TYPE "G" CURB
TYPE "E" INT.
TYPE "E" CURB
2’ – 11 7/8”
16”
28”
22”
2’ – 11 7/8”
16”
3’ – 3”
12”
2’ – 11 7/8”
2’ – 0”
12”
1’ – 6”
2’ – 6”
PRODUCED FROM 1950 TO 1952
LENGTHS: 16’, 20’ & 28’
PRODUCED FROM 1953 TO 1960
LENGTHS: 20’ & 28’
PRODUCED FROM 1952 TO 1965
LENGTHS: 30’, 35’, 40’ & 42’

## Slide 13
Reinforced Concrete
Girders
2’ – 11 7/8”
20”
1’ – 9”
12”
2’ – 11 7/8”
22”
12”
1’ – 9”
Superstructure Elements
TYPE "HC" INT.
TYPE "HC" CURB
TYPE "VH" CURB
PRODUCED FROM 1961 TO 1974
LENGTHS: 20’, 28’, 33’ & 38’
PRODUCED FROM 1974 TO 1979
LENGTHS: 20’, 28’, 33’ & 38’
TYPE “VH" INT.

## Slide 14
Prestressed Concrete
Girders
3’ – 11 1/2”
20”
2’ – 5 3/4”
1’ – 8”
13 3/8”
20”
1206
510
510
340
756
510
Superstructure Elements
PRODUCED FROM 1974 TO 1979
LENGTHS: 20’, 25’, 30’ & 35’
PRODUCED FROM 1979 TO 1990
LENGTHS: 6, 8, 10 & 11 m
TYPE “VS” INT.
TYPE “VS” CURB
TYPE “SM” INT.
TYPE “SM” CURB

## Slide 15
Prestressed Concrete
Girders
Superstructure Elements
CURRENTLY IN USE
LENGTHS: 6, 8, 10, 12 & 14 m
LENGTHS: 6, 8, 10 & 12 m
LENGTHS: 6, 8, 10 & 12 m
1206
510
510
340
356
510
510
1206
350
50
510
1206
350
50
TYPE "SC" INT.
TYPE "SC" EXT.
TYPE "SC" INT.
TYPE "SC" EXT.
TYPE "SL" INT.
TYPE "SL" EXT.

## Slide 16
Superstructure Elements

## Slide 17
Superstructure Elements

## Slide 18
Superstructure Elements
SKEW ANGLE
BRIDGE
SKEW ANGLE "LHF"
C
C
BRIDGE
BRIDGE
STREAM

## Slide 19
900
Hazard Marker
  Warning sign at bridge approaches.
  Yellow board with black sloping lines.
  Placed at end of the bridge, in line with railing posts.
Superstructure Elements

## Slide 20
Bearings
  Neoprene or rubber pads or strips.
  Used over steel and concrete caps.
  Transmit all loads from superstructure to substructure.
  Permit longitudinal movement of the superstructure.
  Allow rotation caused by deflection.
Superstructure Elements

## Slide 21: Substructure Elements
Substructure comprises of all elements below bearings.
Major components:
  Abutments
  Pier or Pile Bent (H pile pier or Pipe pile pier)

## Slide 22: Substructure Elements
Other components:
  Caps & Subcaps.
  Piles.
  Sheathing & Bracing.
  Wingwall
  Backwall
  Riprap

## Slide 23: Substructure Elements
Substructures can be:
  Timber piles with timber cap
  Timber piles with steel cap
  Steel “H” piles with steel cap
  Steel “H” piles with concrete cap
  Steel pipe piles with concrete cap

## Slide 24
SPILL THROUGH ABUTMENT
HIGH BACKWALL ABUTMENT
ABUTMENT CAP
CAP SPLICE
TIMBER SCAB
BACKWALL
HEAVY ROCK
RIPRAP
WINGWALL
WINGWALL
PILE
ABUTMENT SUBCAP
ANCHOR PILES
ABUTMENT PILES
Substructure Elements

## Slide 25
Substructure Elements
Timber Piers ( 2 Types
Of Bracing)
PIER CAP
CAP SPLICE
SUB CAP
WITH SWAY BRACING
WITH PLANKING
STRUTS
MAXIMUM HEIGHT FOR A
SINGLE ROW OF PILING IS 3.0 m

## Slide 26
Substructure Elements
DECK SURFACE
STEEL NOSE
STEEL BRACING
GALVANIZED STEEL
H-PILES
HIGH BACKWALL ABUTMENT
PIER
(HALF VIEW ONLY)
(HALF VIEW ONLY)
STEEL CAP
STEEL H PILE SCAB
STREAM BED
3.0 m MAX.
6.0 m MAX.

## Slide 27
STEEL CAP
TIMBER PILES
SPILL THROUGH ABUTMENT
PIER
HALF VIEW ONLY
HALF VIEW ONLY
DECK SURFACE
PLANK SHEATING
WINGWALL PILE
STEEL CAPITAL
STREAM BED
3.5 m MAXIMIM
1.25 m MAXIMIM
Substructure Elements

## Slide 28
(HALF VIEW ONLY)
(HALF VIEW ONLY)
PIER
ABUTMENT
DECK SURFACE
GALVANIZED STEEL
H-PILES
GALVANIZED PIPE
PILES
CONCRETE WINGWALL
CONCRETE PIER CAP
STREAM BED
1.0 m
MAX
6.0 m
MAX
Substructure Elements

## Slide 29
Substructure Elements
2.5 m
MAX
SC PRESTRESSED CONCRETE GIRDER BRIDGE WITH STEEL SUBSTRUCTURE
HIGH ABUTMENT BACKWALL (ELEVATION)
GALVANIZED STEEL
H-PILES
GALVANIZED STEEL CAP

## Slide 30
Substructure Elements
SC PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE (SECTION)
GALVANIZED STEEL CAP
HP 310 X 94
T.T NAILING STRIP
BOLTED TO PILE
T.T PLANKING
FILTER FABRIC
SC GIRDER
DOWEL
NEOPRENE PAD
GALVANIZED STEEL PILE
HP 310 X 94
C
ABUT. &
PILES

## Slide 31
Substructure Elements
SC PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE PIER (ELEVATION)
STEEL CAP
STEEL NOSE
U/S
PILE
BRACING
GALVANIZED STEEL
PILES
5.5 m
MAX
2.5 m
MAX

## Slide 32
Substructure Elements
SC PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE PIER (ELEVATION)
GALVANIZED STEEL CAP
2 - HP 310 X 94 C/W STIFFENER
PLATES
SC GIRDER
DOWEL
NEOPRENE PAD
GALVANIZED STEEL PILE
HP 310 X 94
C
PIER
PILES
SC GIRDER
ASPHALT
FIBRE BOARD

## Slide 33
CULVERTS

## Slide 34
CULVERT
ROADWAY
STREAMBED (U/S)
CONCRETE SHOULDER
(OR COLLAR)
CONCRETE HEADWALL
CONCRETE
CUT-OFF WALL
BARREL SECTION
BEVEL END
BEVEL END
U/S INVERT
CLAY SEAL
(BOTH ENDS)
INLET
OUTLET
RIPRAP
STREAMBED (D/S)
D/S INVERT
APRON
CROWN OF ROAD
LONGITUDINAL SECTION THROUGH CULVERT
Culvert Components
C

## Slide 35
SPAN
RISE
ROAD SURFACE
CULVERT
TOP PLATES
(ROOF OR TOP ARC)
SIDE PLATES
(WALL OR SIDE ARC)
BOTTOM PLATES
(FLOOR OR BOTTOM ARC)
INVERT
SECTION
Culvert Components
C

## Slide 36
COLLAR
ARCH
(HEADWALL)
APRON
INVERT
CUT-OF-WALL
COLLAR
ARCH
(HEADWALL)
CUT-OF-WALL
Culvert Components

## Slide 37
SQUARE FLUSH
INLET
SQUARE PROJECTING
INLET
BEVEL FLUSH
INLET
BELL-MOUTH
INLET (PLAN)
Typical Inlet Configurations

## Slide 38
H1
H2
SEEPAGE
F
Uplift force, F is proportional to H1 – H2
Seepage is proportional to H1 – H2
Concrete End Treatment

## Slide 39
w
F
Headwall
Shoulder
Cut-off-wall
Concrete End Treatment

## Slide 40
Concrete end treatment has five important functions:
  Weight provides downward force to resist uplift.
  Cut-off wall lengthens the seepage path.
  Shoulder strengthens the bevel edges.
  Enhances the inlet transition.
  Aesthetics.
Concrete End Treatment

## Slide 41
Problems due to seepage:
  Fine material is removed from the granular backfill.
    Loss of material creates voids.
    Support length of the backfill is reduced.
    Culvert can deform.
  Uplift forces are increased.
Clay Seals

## Slide 42
Clay Seals
CLAY SEAL (EACH END)

## Slide 43
Flowing water causes shear forces on the bed.
  Shear force is proportional to velocity.
  High shear forces will erode bed and bank material.
    Causes fill stability problems at inlet and outlet.
    Causes structural deformation.
Scour Protection - Aprons

## Slide 44
Riprap is placed to protect the end of culverts.
Larger and heavier riprap provides higher shear resistance.
Cut-off wall helps anchor riprap.
Scour Protection - Aprons

## Slide 45
Culvert (SPCSP) Installation

## Slide 46
Culvert (SPCSP) Installation

## Slide 47
END