## Slide 1: CULVERT INSPECTION & RATING

## Slide 2: Introduction
Approximately 63% of all structures are culverts
Bridge sized culverts have an equivalent diameter of 1500mm or greater
May also inspect if multiple small culverts are equivalent in hydraulic capacity to bridge-sized (e.g. 2-1200mm)
May inspect certain other non-bridge sized culverts if several (e.g. LL Xing)

## Slide 3: Introduction
Many different types of culverts – refer to Table 1.1 in Manual
Vast majority are CSP or SPCSP in various shapes - round, arch pipe, horizontal and vertical ellipse
Three culvert forms (Cul1, CulE, CulM)
Same forms used for all types of culverts except for Timber pipe (TP) which is inspected using a TT form

## Slide 4: Form Types
CUL1
  Single culvert or single culvert extended with same material and size
CULM
  Two or more culverts (MP, SP or BP etc.)
  Includes 1 Upstream & 1 Downstream End section for each Barrel section
  Exception is Concrete Boxes (BP) - single U/S & D/S section for all barrels
  Includes 2 cell box extended with single steel
CULE
  Single culvert extended with different material and/or size
  One U/S section, 2 or more Barrel sections and one D/S section
  Original and extended barrels inspected and rated separately

## Slide 5: Inventory Information
Extracted from BIS
Span/Rise is original design shape
If round, then only Rise is recorded as shown in example above
Span types – refer to Table 1.1 and Sec. 13.2.3
Corrugation Profile and Plate Thickness selected from Table 13.1 and 13.2 (Manual)
Specific information is provided for all pipes
If original design shape unknown or in question, inspector should consult CPI handbook and/or use the average of the U/S and D/S span and rise measurements.

## Slide 6: Culvert Span Types

## Slide 7: Numbering and Identification
Where the culvert does not carry flow determine “upstream” and “downstream”
  Look in direction of increasing chainage
    (to north or east)
  Left is “upstream” (end 1)
  Right is “downstream” (end 2)
  Keep same choice for each subsequent inspection

## Slide 8: Numbering and Identification
North or East
South or West
“Downstream” End 2
“Upstream” End 1
2
1

## Slide 9: Numbering and Identification
Primary span is the largest span at the site
Secondary span is the smaller span
Multiple culverts of same dimension are numbered in order of increasing chainage (from south to north or west to east)
Multiple culverts also have same Ring numbering system (R1, R2, R3, etc.)

## Slide 10: U/S and D/S Ends - General
Individual rating sections for the Upstream and Downstream ends
Single upstream and downstream end sections for the CUL1, CULE forms
Separate Upstream and Downstream ends for each Barrel section on CULM forms - except Concrete Boxes. Note in explanation of condition which barrel is being inspected (i.e. south, west, #1)
Upstream and Downstream sections are identical
Items are inspected and rated the same way for both ends

## Slide 11: U/S and D/S Ends - General

## Slide 12: U/S and D/S Ends - End Treatment
Purpose:
  Improve hydraulic performance
  Prevent undermining due to scour
  Prevent scour of the embankment
  Reduce piping along or under the culvert
  Resist uplift due to buoyancy forces
  Shorten the culvert
  Stiffen the ends
  Improve aesthetics

## Slide 13: End Treatment -Types
Steel
  Most common
  Bevel end with no concrete treatment
Concrete
  Presence of any or all of: Headwall, Collar, Wingwall, Cutoff Wall
Other
  Timber Culvert with Timber End Treatment
None
  Square end – no Bevel present

## Slide 14: Bevel Ends – End Treatment Type is “Steel”

## Slide 15: Bevel Ends with Full Concrete End Treatment - Type is “Concrete”

## Slide 16: Bevel End with Full Concrete End Treatment (headwall, collar and cut-off wall) - Type is “Concrete”

## Slide 17: End Treatment - Headwall
Located over the crown
Usually attached to the barrel
Purpose:
  Aesthetics
  Strengthen end
  Resist buoyancy force
  Retaining walls

## Slide 18: End Treatment - Headwall
Look for:
  Signs of movement or tilting
  Loose connections
Rate according to condition of material and functionality of component
Condition affecting functionality rate 4 or less

## Slide 19: End Treatment - Collar
Located along the beveled slopes of flexible culverts between headwall and cutoff wall
Usually constructed from concrete
Usually used with and connected to headwall and cutoff walls
  May be used alone

## Slide 20: End Treatment - Collar
Purpose:
  Stiffen the bevel
  Resist buoyancy force
  Improve hydraulic efficiency of inlet or outlet
  Concrete slope protection
    protect against scour / erosion
    reduces piping potential
    works in conjunction with rip rap

## Slide 21: End Treatment - Collar
Look for:
  Evidence of piping or scour / erosion
  Loose connections
  Voids underneath or settlement
Rate according to condition of material and functionality of component
If not connected to culvert, rate 4 or less
If piping, rate 4 or less:
  Also rated under bevel end and barrel

## Slide 22: End Treatment - Wingwalls
Generally found at culverts that do not have bevels
Shape is either Parallel, Perpendicular, or Flared to culvert axis
Main difference from Bevel is Wingwall is not attached to the barrel
Usually constructed from concrete or steel
Purpose
  Improve hydraulic efficiency
  Retain embankment fill

## Slide 23: End Treatment - Wingwalls
Record Shape as “Parallel”, “Flare”, or “Perpendicular” (to culvert axis)
  Parallel wingwall
    Req’ less scour protection between walls
  Flared wingwalls
    more hydraulic efficient
May have a reinforced concrete slab between
  Prevents undermining of wingwalls due to scour
  Act as struts for greater stability
  If slab is present rate with wingwalls

## Slide 24: End Treatment - Wingwalls
Look for:
  Evidence of movement
  Loose connections (gap at barrel)
  Scour / erosion at toe or behind wingwall
If wingwall is unstable rate 4 or less
Separation losing fill rate 4 or less
Includes rating of wingwall floor slab

## Slide 25: End Treatment – Flared Wingwalls

## Slide 26: End Treatment - Cutoff Wall
Located at the end of the culvert
Vertical wall extending down below the invert of the pipe
Depth exceeds the depth of the riprap or concrete apron
Usually constructed from concrete or steel
Purpose:
  Reduce potential for undermining of end of culvert
  Minimize possibility of piping
  Resist buoyancy force

## Slide 27: End Treatment - Cutoff Wall
Look for evidence of:
  Undermining
  Piping
  Uplift
  Loose connections
Usually not possible to inspect since they are submerged or covered with ice or debris
  If not visible rate “N”
  If certain not present rate “X”
If piping, rate 4 or less
  May also affect Bevel End and Barrel Rating

## Slide 29: End Treatment - Bevel End
Sloped section at the end of the culvert
Permanently attached to the barrel
Generally parallel to the culvert axis
Bevel types
  Full bevel
  Step bevel

## Slide 30: End Treatment - Bevel End
Compared to projecting ends, bevel ends are more:
  Aesthetic
  Economical
  Hydraulically efficient
Compared to projecting ends, bevel ends on corrugated steel culverts are more flexible and susceptible to:
  Deform due to lateral earth pressure
  Uplift due to buoyancy
  Heave due to frost action

## Slide 31: End Treatment - Bevel End
Measure or estimate heaving of bevel and record amount
Often best place to estimate is from inside barrel looking back to Bevel
Use waterline as level
Some heave is tolerable as long as water is entering Bevel

## Slide 32: End Treatment - Bevel End
If possible, measure or estimate height above or depth below streambed and record amount in mm. (may not be able to measure or confirm measurements in high water or winter).
Normally “Below” as designed to be buried ¼ diameter below streambed.
If invert is “at streambed” record Above/Below as 0mm.
Find a representative natural streambed location
  Discount presence of localized scour hole or deposits (aggrading) at end of culvert

## Slide 33: End Treatment - Bevel End

## Slide 34
Look for:
  Piping
  Deformation
  Impact damage
  Corrosion that affects strength
  Abrasion
If piping, rate 4 or less
  Also rated under End Treatment if present
Defects/deformations not affecting function rate 6 or less (un-supported bevel - no heave)
Severe corrosion affecting strength (perforations) rate 4 or less – otherwise corrosions should not affect rating
If no bevel, rate “X”
  Ped and cattle underpasses often have square ends
End Treatment – Bevel End

## Slide 35: Bevel End – Severe misalignment due to buoyancy forces
35

## Slide 36: Scour Protection
Usually, heavy rock riprap
The current version of Std. Drawing S-1418-20 shows the minimum requirements for riprap
  Coverage
  Size
  Minimum thickness
  Gradation
  https://www.alberta.ca/assets/documents/trans-bridge-culverts-drawings.pdf

## Slide 37: Scour Protection
Purpose is to prevent scour and erosion at culvert ends which may:
  Undermine the culvert
  Undermine the sideslope
  Cause the formation of sand bars

## Slide 38: Scour Protection
Record the type of Scour Protection
  Rock, bagged concrete, concrete, gabion baskets, geotextile mats, MSE wall, natural
  If none exists and none is required, record type as “NATURAL”
  If none exists but is required, record type as “NONE”
Estimate and record the average size (rock only)
Look for:
  Durability of riprap - e.g., sandstone is not acceptable
  Shape – flat rocks not desirable
  Displacement or movement
  Scour
  Current standards on S- 1418

## Slide 39: Scour Protection Ratings
No scour/erosion or displacement rate 7 or more
If none exists and none is required record type as “NATURAL” and rate 7 or more
If none exists but is required record type as “NONE” and rate 3 or less and make recommendation)
Generally, not rated higher than Scour rating – especially when Scour is 4 or less
Protected area is smaller than required or rock gradation or quality is inadequate rate 4 or less
Concrete protection with excessive settlement or undermining rate 3 or less
Cattlepasses that also handle drainage rate – otherwise X

## Slide 40: Scour / Erosion
Removal of material from the streambed, banks or sideslopes by the action of flowing water and/or constrictions or obstructions
Effects:
  Undermine the culvert
  Undermine the sideslope and/or road embankment
  Alter culvert hydraulics
  Impede fish passage

## Slide 41: Scour / Erosion
Two types:
  General – uniform lowering of original stream
  Local – occurring at specific locations
Look for:
  Scour holes, especially at downstream ends
  Undermining of culvert end or sideslope
  Slumping of sideslope or banks
  Areas where flow impinges on banks, sideslopes or protection systems
  Areas susceptible to high velocities and undermining
    culvert footings
    ends or bottoms of wingwalls and cutoff walls
    sides of collars
    ends or bottoms of protection systems

## Slide 42: Scour / Erosion
Rate the presence and extent of scour and adverse effects on culvert, embankment, streambed and banks
If culvert and embankment are not affected, rate 5 or more
Scour/erosion affecting culvert, rate 4 or less

## Slide 43: Scour / Erosion

## Slide 44: Scour Protection

## Slide 45: Beaver Activity
Beavers frequently construct dams at inlet or inside culverts
Effects:
  reduced flow capacity
  Flooding upstream
  Scour
  Ponding of water inside culverts preventing inspection

## Slide 46: Beaver Activity
Indicate the presence of beaver dams in or near the culvert by Yes or No
If “yes”, provide comment
No rating required but may affect
  End General Rating
  Scour
  Waterway Adequacy in Barrel section

## Slide 47: U/S & D/S End General Rating
Governing elements: (Refer to 1.10.7 & 13.5.10)
  Headwall
  Collar
  Wingwall
  Cutoff Wall
  Bevel end
  Scour protection
  If all are rated “X” then provide rating based on general condition of culvert end

## Slide 48: Barrel - Rigid Types
Made from concrete or timber or heavy wall steel pipe
Designed to carry loads without deflection (Rise and Span measurements normally not necessary).
Culvert carries entire load with no reliance on surrounding fill for support.
Generally, more expensive but more durable, last longer and require less structural maintenance.

## Slide 49: Barrel - Flexible Types
Made from corrugated steel
Low strength as a stand-alone structure
Dependent on surrounding backfill for support
Culvert deflects under load until the backfill picks up the stress
Entire load carrying system cannot be inspected directly (I.e., can inspect culvert but not backfill)
Flexible culverts more susceptible to failure by:
  Change in shape due to excessive deflection
  Defective joints - cracks, open joints, cusped seams, etc.
  Severe corrosion
  Uplift of ends due to buoyancy forces

## Slide 51: Barrel - General
If barrel is accessible record current date
If barrel is not accessible explain why, take photograph showing condition & retain the previous “last accessible date”. Then 3 possible rating scenarios:
  If the previous critical elements (roof, sidewall, longitudinal seam) ratings were 7 or higher AND the inspector is able to get good sight lines down the barrel from both ends to confirm the shape, the previous roof, sidewall, and Barrel General ratings can all be carried forward.
  If previous roof or sidewall ratings were 6 or less, barrel elements and General Rating are rated N (not visible). Previous comments are retained and dated.
  If previous critical element and Barrel General ratings were 4 or less, elements are rated N with comment indicating previous rating and Gen Rating carried over
If more than one barrel indicate location (west) or span number

## Slide 52: Barrel - Special Features
Cannot be rated under another component
May be temporary or permanent
Must be visible to inspect
  Special design features sometimes not inspectable (ribs, thrust blocks, etc.)
If birds nest present in barrel, note in Explanation of Condition

## Slide 53: Barrel - Special Features
Common Examples
  Struts
  Shotcrete beams
  Concrete Floor
  Storm Drains
  Elbow
  Beaver Control Device
Record type
Provide additional information in Explanation of Condition
  Description
  Location
  Dimensions
Provide rating based on condition /functionality

## Slide 54: Barrel - Special Features Shot-crete Beam

## Slide 55: Barrel - Special Features Struts – Rated 3

## Slide 56: Barrel - Deformation

## Slide 57: Barrel - Ring
Different elements make up a complete ring:
  Roof
  Sidewall
  Floor
  Bolted or riveted seams
  Circumferential seams (bolted (SPCSP) or external coupler (CSP))
Purpose:
  Carry water flow or traffic
  carry loads and transmit to surrounding soil
  Prevent infiltration of fill

## Slide 58: Barrel - Ring
120
120
60
60
Floor
Roof
S
i
d
e
w
a
l
l
S
i
d
e
w
a
l
l
For round culverts, use approximate arcs shown
  Use longitudinal seam if close

## Slide 59: Barrel – Ring Defects
Flexible Steel culverts look for:
  Deformation (measure crest to crest)
  Localized crimping or buckling
  Longitudinal seam problems
  Corrosion
  Abrasion on floor or lower sidewall
Rigid Timber culverts look for:
  Material defects – rot decay
Rigid Concrete culverts look for:
  Structural problems - cracking
  Material defects - corrosion, scaling, freeze-thaw damage

## Slide 60: Barrel - Roof
Flexible Culverts:
Record lowest measured Rise in mm (crest-crest). Mark in culvert for future reference if deflections are ≥7%.
Record Ring number where measurements taken.
If floor bulge occurs at same location add bulge to measured rise and explain in comments.
Calculate and record Sag in mm (design rise – measured rise).
Calculate and record % Sag (rounded up or down – e.g. 5.4% is recorded as 5%).
Rate Roof based on % Sag (Table 13.3) or other visual defects.
If not able to measure Rise due to ice, silt, concrete floor, etc. a Roof rating is still required based on visual evidence and estimated sag.

## Slide 61
Flexible culverts - continued
Presence of temporary repairs has no influence.
Sag 5% or <, no corrosion – rate 7
Sag within 7%, corrosion with pitting - rate 5
Sag within 10% – rate 4
Sag 11-15% or isolated perforations – rate 3
Sag >15%, roof flattening, reverse curvature, or extensive perforations – rate 2.
Reverse curvature in flat HE or round under low cover, severe perforations – rate 1.
Consider Longitudinal Seam rating if in Roof.
Rigid Culverts:
Rate Roof based on visual evidence, defects
Measurements not required
Barrel – Roof Ratings

## Slide 62: Barrel – Roof Ratings Reverse Curvature-Rated 2

## Slide 63: Barrel - Sidewall
Flexible Culverts:
Record greatest measured span in mm. (crest-crest). Mark in culvert for future reference if deflections are ≥7%.
Record Ring number measurements taken.
Calculate and record Deflection in mm (measured span – design span).
Calculate and record % Deflection (rounded up or down (e.g. 7.7% = 8%)
Rate Sidewall based on % Deflection (Table 13.3) or other visual defects.
If not able to measure span due to size, ice, etc. a sidewall rating is still required based on visual evidence and estimated deflection.

## Slide 64
Deflection within 5%, no corrosion - rate 7
Deflection within 7%, corrosion with pitting - rate 5
Deflection within 10% – rate 4
Deflection 11-15%, crimping or buckling, isolated perforations – rate 3 or less.
Deflection >15%, crimping/buckling with plate shear, extensive perforations – rate 2 or less.
Consider Longitudinal Seam rating if in Sidewall (e.g. - Longitudinal Seam in Sidewall rated 2 governs Sidewall rating).
Rigid Culverts:
Rate Sidewall based on visual evidence, defects
Measurements are not required
Barrel – Sidewall Ratings

## Slide 65: Barrel Sidewall Severe Inward Movement

## Slide 66: Barrel – Sidewall Buckling Rated 3 or less

## Slide 67: Barrel - Floor
Check timber floors for rot, missing sections.
Check concrete floors for cracking, spalling, missing sections.
Check steel floors for cracks, crimping/buckling, defective seams, corrosion, abrasion.
Measure or estimate floor bulge and record ring number.
For flexible culverts - If greatest floor bulge is occurring in same ring as worst roof deflection add bulge to measured Rise
Indicate abrasion on floor by Yes or No. If yes, provide a comment.

## Slide 68: Barrel - Floor
Rate flexible culvert floors as per Table 13.3:
  Isolated perforations rate 4
  Extensive perforations rate 3
  Severe perforations rate 2
  <5% bulging, minor abrasion and corrosion, no buckling or seam defects rate 6 or more
  Seam rating may govern if located in floor

## Slide 69: Barrel - Ring

## Slide 70: Barrel - Circumferential Seams
Refers to seams joining individual rings or sections of culvert
Found on most types of culverts
  Bolted seams on SPCSP
  Couplers on CSP or Riveted pipes
  Joints in precast concrete
  Construction joints in cast-in-place concrete

## Slide 71
Purpose
  Join rings
  Prevent infiltration of backfill
Most common problems are separation caused by settlement or corrosion of couplers
  Especially CSP and precast concrete (settlement)
Potential for safety problem if void develops in fill
Look for:
  Separation
  Loose or missing couplers (corrosion)
  Bent or broken edges on the rings
  Misalignment of rings
  Infiltration of backfill
  Voids in surrounding fill
Barrel - Circumferential Seams

## Slide 72: Barrel - Circumferential Seams
Record width of worst separation.
Misalignment with visible fill but no soil infiltration - rate 4 or less.
Misalignment or seperation with minor soil infiltration - rate 3 or less.
Void in backfill from loss of material due to soil infiltration - rate 2 or less.
Severe loss of material due to soil infiltration - rate 1.
Cracking from over torquing of bolts but no growth or problems – rate 5.
Cracking due to roof sag rate 4 or less.
May affect Roof, Sidewall or Floor rating if severe (2 or less).

## Slide 73: Barrel - Circumferential Seam Material Loss and Void Rated 2

## Slide 74: Barrel - Circumferential Seam – Visible fill and minor loss but no void - Rated 3 or less

## Slide 75: Barrel - Longitudinal Seams
Applies to SPCSP and CSP culverts with riveted seams
All others, Rate “X”

## Slide 76
Purpose
  Join individual plates in ring
  Transmit loads between plates
  Approx. 75% bending strength of plates
Indicate if all seams properly lapped by Yes or No
  If No, provide comment
Indicate if seams staggered by Yes or No
  Within same arc only
  At change of arc should not be staggered
  If No provide comment
  Most common problem is cracking
  Especially on improperly lapped seams
Barrel - Longitudinal Seams

## Slide 77: Barrel - Longitudinal Seams
Typical longitudinal seams
INCORRECT LAP
CORRECT LAP

## Slide 78: Typical longitudinal seams
Cracked Seam

## Slide 79: Barrel - Longitudinal Seams Cracked Seams
Record and comment on number of rings with cracked seams
Record and comment on number of rings with 2 or more cracked seams (may cause catastrophic failure)
Record least remaining steel between cracks and record location in comments (“65 mm rem. steel at R9 west sidewall”)
Mark and date ends of worst cracks – pencil is best for marking ends of cracks. Record measurements with lumber crayon or sharpie.
Properly lapped seam has bolt in valley nearest visible edge of plate

## Slide 80: Barrel - Longitudinal Seams Other Problems
  Poorly nested plates
  Improper fabrication and/or poor assembly
  Cusping
  Sharp break or discontinuity in curvature
  Occurs most often at longitudinal seams
  Improper fabrication , poor assembly/plate rotation during torqueing
  Improper backfill
  Bolt tipping
  High ring compression causing plate slippage and/or hole elongation
  Plate distortion
  High ring compression, improper assembly and backfill
  Corrosion

## Slide 81: Barrel - Longitudinal Seams Rating
Rate as per Table 13.3
All seams properly lapped and no defects rate 9
Seams are not properly lapped but in otherwise excellent condition - rate 7
>100mm remaining steel between cracks rate 4
50 – 100mm remaining steel between cracks - rate 3
<50mm remaining steel between cracks rate 2
Two or more cracked seams in same Ring – rate 2
Rating for longitudinal seams also affect Roof, Sidewall and Floor ratings
Rate riveted longitudinal seams in CSP

## Slide 82: Barrel – Wrong Lap and Cracked Longitudinal Seam with <50mm Remaining Steel - Rated 2

## Slide 83: Barrel – Cracked Longitudinal Seam/Wrong Lap <100mm and >50 mm Remaining Steel – Rated 3

## Slide 84: Barrel – Cracked Longitudinal Seam and Wrong Lap

## Slide 85: Barrel – Failed Longitudinal Seam

## Slide 86: Cracks in Properly Lapped Seam Bolt in valley is closest to visible edge

## Slide 87: Barrel - Coating
Applicable to steel culverts only
Applies mainly to zinc or aluminized coating
  Can include other types – bituminous, polymer
Purpose is to protect the steel from corrosion
  Zinc & aluminum protect by sacrificial action

## Slide 88: Barrel - Coating
Corrosion can occur on soil or water side of culvert
Soil side corrosion is generally visible above waterline and first visible at the seams
  Can lead to perforations
  Difference in backfill resistivity
  Corrosive chemicals in backfill or water in fill
Water side corrosion usually occurs in lower sidewall and floor areas
  Abrasion can remove protective coating
  Water may have low pH or contain corrosive chemicals from agriculture
  Anaerobic bacteria may live in stagnant water

## Slide 89
Look for:
  Fabrication or installation defects or damage
  Loss of coating - Corrosion
  Rust stains from bolt holes or seams
  Perforations
Record if corrosion is on SOIL and/or WATER side – provide comment if Yes
Rate according to Table 13.3
Superficial corrosion no pitting – rate 5 or 6
Corrosion with pitting in roof, sidewalls, or floor rate 4
Isolated perforations in roof or sidewall, extensive perforations in floor - rate 3
Extensive perforations in roof or sidewall, severe perforations in floor - rate 2
Severe perforations in roof or sidewall - rate 1
Rating of Coating may affect other elements ratings
Barrel - Coating

## Slide 90: Barrel Coating – Lineal Sidewall Perforations – Rated 2

## Slide 91: Barrel Coating – Severe Floor Perforations – Rated 2

## Slide 92: Barrel - Camber
Refers to longitudinal grade line of invert
No rating is required
If water line is level can be used to determine camber
Record whether camber is POSITIVE, Zero (0), or NEGATIVE
If significantly POSITIVE or NEGATIVE provide Explanation

## Slide 93: Barrel - Camber

## Slide 94: Barrel – Fish Passage Adequacy
No longer rated.
The previous rating and information from the last inspection may be on the form.
Change rating to X.
Cross out / remove comments from the Explanation of Condition.
x
x

## Slide 95: Barrel – Fish Passage Adequacy
Types of baffles
  Spoilers
    Concrete or steel projections
  Large boulders
  Weirs
    Extend fully across floor
    May have notches
  Bolted to floor to prevent displacement
Record type of baffle or NONE. Rate the condition and functionality of baffles including anchorages

## Slide 96: Barrel - Waterway Adequacy
Refers to the ability of the culvert to safely pass the design flow
  Maintain Freeboard
  Pass drift without damage
  No damage from backwater created

## Slide 97: Barrel - Waterway Adequacy
Adequately sized culvert may be affected by:
  Ice build up
  Silt deposition
  Drift accumulation
  Beaver dams
  Ponding
  Repair or rehabilitation work
    Shotcrete beams
    Struts

## Slide 98: Barrel - Waterway Adequacy
Indicate presence of ice build up (icing) by Yes or No if Yes explain
  Freezing of ponded water
  Results from active springs which freeze and causes layers of ice to build up
  If previously Yes - leave and retain comments adding date of previous inspection
Indicate presence of silt build up (Silting) by Yes or No, if Yes explain
  Invert normally below streambed
  Minor accumulation of silt expected
Indicate presence of drift in Barrel by Yes or No
If “yes”, explain

## Slide 99: Barrel - Waterway Adequacy
Look for:
  High water marks (not normal flow lines)
  Potential damage from backwater
  Potential for drift
  Evidence of high velocities
    Scour
    Silt deposition downstream
  Presence and effect of items which can affect adequacy

## Slide 100: Barrel - Waterway Adequacy
100
Rate “X” if not a drainage culvert (cattlepass, pedestrian underpass)
Rate if cattlepass also handles water flow
Adequate opening rate 5 or more
HWM above crown, 4 or less
Culvert blockage 50% or more rate 3 or less

## Slide 101: Barrel - Waterway Adequacy - 100% Blockage

## Slide 102: Barrel - Waterway Adequacy - 50% Blockage

## Slide 103: Barrel - General Rating
Governed by the following element ratings (refer to 1.10.8 and 13.6.14)
  Roof
  Sidewalls
  Longitudinal seams
  Floor rating of 3 or less
  Circumferential seam rating of 2 or less
  Corrosion rating of 2 or less
  Waterway adequacy rating of 2 or less

## Slide 104: Barrel Not Accessible – Critical Element & General Rating
If barrel is not accessible for inspection – 4 possible rating scenarios
Previous Roof, Sidewall, and Barrel General ratings ≥7 AND can obtain sightline of barrel from ends to confirm shape, then previous Roof, Sidewall, and Barrel General ratings are carried forward with comments. Longitudinal Seam is rated N with comment indicating previous rating (e.g. P.R. 8)
Previous Roof, Sidewall, and Barrel General ratings are 5 or 6. Rate barrel elements and Barrel General rating “N”
Previous Barrel General Rating are 4 or less, then barrel elements are rated N and previous General Rating of 4 or less is carried forward with comment indicating “Gen. Rating carried forward”
3. Previous Roof, Sidewall, Longitudinal Seam and Barrel General ratings are 5 or 6, rate barrel elements and Barrel General Rating “N”

## Slide 105: Barrel Not Accessible – Critical Element & General Rating
If barrel is not accessible for inspection – Continued
4. Previous Roof, Sidewall, and Barrel General ratings are 5 or more but obvious defect or change noted when viewed from ends (e.g. roof deflection). Reduce applicable element rating and General Rating based on visual evidence and recommend inspection during low water/winter, or Level 2 de-water inspection
Refer to Section 13.6.2 for further information
Barrels not accessible for 2 consecutive inspections recommend inspection during low water/winter, or Level 2 de-water inspection. Refer to 13.9.1.5

## Slide 106: Effects of Struts on Barrel General Rating
Inspector may increase General Rating by 1 or 2 points but not exceed rating of 4.
Conditions for increase to rating:
  struts in place more than 2 years (permanent repair)
  struts rated 5 or more
  1 permanent reference point for future monitoring
  struts inspected after any significant event
  consider culvert size and depth of cover (failure of large diameter culvert under high fill may not be as serious as under low fill)
  does not apply when deflections >30% or cracked seams with less than 25mm remaining steel
  applied to general rating only, element ratings remain unchanged

## Slide 107: Questions?