## Slide 1: SUPERSTRUCTURE INSPECTION AND RATING

## Slide 2
Superstructure is the portion of the bridge above the caps
Purpose
  Carry traffic
  Transfer loads to substructure
Component materials
  Timber
  Concrete
  Steel
  Combination
Superstructure Components:
  Bearings
  Stringers or girders
  Deck or subdeck
  Deck joints
  Deck wearing surface
  Drains
  Curbs or Wheel Guards
  Bridgerail
  Sidewalks (if present)
Introduction

## Slide 3: Standard Girder Bridge

## Slide 4: Timber Bridge
Subdeck

## Slide 5
Two form types;
  TT – treated timber bridges
  PCS - Standard precast bridges (either plain reinforced or pre-stressed)
Both are tailored for components in each type of bridge
Introduction

## Slide 6: Material Defects

## Slide 7
Decay
caused by fungi
needs moisture, oxygen and conducive temperature
pressure treatment delays growth
look for discoloration (white stains coming from cracks, dampness of wood, ring shrinkage at end grain, hollow sounds, change in geometry
look in areas likely to retain moisture
  bearing or contact areas, buried timber
look in areas where treatment is broken/cut
  bolts, drifts, dowels, cuts, cap ends
Material Defects - Timber
Structural Failure/Degradation
due to loads placed on structural members
overloads, collisions, poor grain pattern
look for cracks, splits, breaks in structural members
  stringers, timber posts, rails, etc.

## Slide 8: Material Defects - Timber
Volume Change
  caused by cycles of wetting and drying creating stress in wood
  look for checks, cracks, warps, twists, etc.
Mechanical Wear
  caused by abrasion from traffic, snowplows, ice flow, debris
  look in area subject to wear/abrasion - deck surface, wheelguard
Fire
  easily recognized
  reduces the load capacity by reducing the effective section of the member
  removes pressure treated zone on the exterior exposing timber to fungal attack

## Slide 11: Timber Defects – Rot

## Slide 12
Timber Defects – Cracked Stringer – Rated 3

## Slide 13
Timber Defects – Cracked Stringer – Rated 3 (+1)

## Slide 14
Timber Defects – Gravel Abrasion

## Slide 15
Timber Defects – Fire Damage

## Slide 16
Structural Cracks
  caused by stresses higher than design
  Flexural – generally not serious unless wide or growing in width
  Shear - most serious - can lead to failure
  Anchorage can be serious depending on cause
Shrinkage Cracks
  caused by rapid drying during hydration
  usually not serious by themselves but let moisture and salt into the concrete (e.g., new conc. deck)
Settlement Cracks
  caused by settlement of the falsework
Map Cracks
  chemical reaction of the aggregate and paste
  usually shallow, from over-finishing
  can cause scaling
Material Defects - Concrete

## Slide 17
Corrosion Cracks
caused by corrosion of steel in the concrete creating delamination's or spalls.
varying widths, locations and orientations
Maintenance or rehab problem
Chipping
caused by external mechanical (grader blade, backhoe arm)
Scaling
caused by freeze/thaw action
related to poor concrete or workmanship
Spalling
caused by corrosion of rebar
Popouts
caused by expansive aggregates
Punchouts
External mechanical that causes tension failure on opposing side
Material Defects - Concrete

## Slide 18: Material Defects - Concrete
Efflorescence
  white salt stains
  may be associated with cracks which allow water to get into concrete
Exudation
  gel-like substance deposited on surface
  may be associated with cracks which allow water to get into concrete
Chemical Attack
  caused by sulfates in the soil reacting with the concrete
  increases the volume of the concrete causing cracks

## Slide 19: Shear Cracks

## Slide 22
Shallow Deck Spall

## Slide 23: SC Girder tops with scaling and section loss

## Slide 24: SC Girder-severe scaling and section loss

## Slide 25: Girder Punchouts

## Slide 27: Material Defects - Steel
Corrosion
  caused by the presence of oxygen and moisture
  reduces section of steel member
  can significantly reduce the load-carrying capacity
  Increases the risk of fatigue failure
  Look in areas prone to the retention of moisture or exposure to salt
    Splash areas, under leaky joints or drains, dirt, and debris accumulation
Cracks
  Caused by fatigue, overload, or collision
  Initially may be too small to be seen by the eye
  can progress rapidly
  look in high-stress or fatigue-susceptible areas
    welds, holes, notches, collision locations, connections, bearing locations

## Slide 28: Material Defects - Steel
Deformation
  caused by fire, collision, overload or thermal stresses
  May be local buckling of part of member I.e., web or flange
  entire member may be bent, twisted or buckled
  look in high stress areas
    collision locations, bearing locations

## Slide 29
TT Form
PCS form

## Slide 30: Special Features
Bridge elements unique to a particular bridge
Which cannot be rated under another element or area of the form
May be permanent or temporary
Lights & WSC station are utilities
Examples include:
  strengthening systems, girder clips
  temporary bents

## Slide 31: Special Features
Record Type(s) – up to 2
Use Explanation of Condition for additional information
  description
  location
  dimensions
Check damage or defects common to the materials and type of component
Provide suitable rating
Make a comment if bird nests are present under the bridge in “Explanation of Condition Field” (e.g., “bird nests at deck underside”)
Refer to Section 7.3 in BIM Manual

## Slide 32: Special Features

## Slide 33: Special Features

## Slide 34
TT forms
PCS forms
PCS (precast or pre-stressed standard)
Wearing Surface

## Slide 37: Wearing Surface
Bonded or fastened to the bridge deck
In direct contact with the wheels of the vehicles
List of types in Section 7.4.2 of the BIM manual
Loose or frozen gravel is not a wearing surface
Purpose
  Protect the deck
  Provide a smooth riding surface
  Provide skid resistance

## Slide 38
TT form combines wearing surface and deck top
  If no wearing surface rating is for deck top only
Verify the wearing surface material type on the report
Record or verify the average thickness in mm
Record the width and thickness of timber planks for TT form
Y/N - is there a lateral connection problem between girders? If Y comment
  HC - bolted connectors; PA - bolted legs; PE - grout keys; PG, HH – none
Wearing Surface

## Slide 39: Standard Girders with Wear Surface

## Slide 40: Wearing Surface - Thickness
Measure at curb
  Most standards curbs 300mm high
  Refer to plans if in doubt
Take readings at ends and midspan, and average
Wearing surface may be thicker at centerline than at curb

## Slide 41
Drive over the deck at fastest safe speed
Observe traffic to assist in rating
Look for material defects
For asphalt pavement wearing surfaces look for:
  cracks (alligator, lane joint, shrinkage and slippage)
  distortion (ruts, depressions and corrugations)
  disintegration (potholes and raveling)
  segregation
Check for delaminations in concrete and asphalt wearing surfaces and record amount in percentage of deck area
Wearing Surface

## Slide 42
If surface is without defects and provides a smooth riding surface with proper skid resistance - rate 9
Asphalt longitudinal cracks rate 7 or less,
If speed must be reduced due to cracks, potholes, etc, - rate 4 or less
If wearing surface does not extend to the curbs and creates a wheel trap - rate 4 or less
Asphalt raveling rate 4 or less
Rutting, potholes or debonding rate 4 or less
Hazardous rate 2
Do not rate down due to excessive thickness (100 mm or more)
  -Lower curb rating if height insufficient
  -Request load rating evaluation
  -Recommend reducing thickness
Wearing Surface

## Slide 43
Record % of surface area with defects and rated 1, 2 or 3 in Detail Rating boxes
Record % of surface area rated N
Wearing surface rated 4 or above, Detail Ratings are “0”
Wearing Surface

## Slide 44: Wearing Surface

## Slide 45: Wide ACP gaps-failed lateral connectors-hazardous WS

## Slide 48: Deck Top
Deck Top is the “structural” part of the deck
The surface on which the wearing surface is bonded
If no wearing surface, the deck top is in direct contact with traffic
Types:
  Cast-in-place concrete
  Precast concrete girders

## Slide 49
Purpose:
  Carry traffic
  Transfer traffic loads to main structural members
  Provide smooth riding surface
  Provide skid resistance
Rated with wearing surface on TT forms
Deck Top

## Slide 50
Listen for unusual noises and look for deflections under traffic
Look for material defects
  Concrete - cracks, scaling, spalling, popouts, abrasion from traffic
  Timber - missing and loose planks, cracks, splits, rot, wear from traffic
Look for unfilled lift and connector pockets on precast girders
Rating of wearing surface does not affect the deck top rating
Deck Top

## Slide 51
Deck smooth, no defects, rate 9
Good condition with hairline cracks, rate 7
If speed reduced due to potholes, etc., rate 4 or less
Record % area rated 3, 2, 1 and N in Detail Rating boxes
Deck top rating 4 or more record 0 in Detailed Rating boxes
Rate 3 or less for severe scaling/spalling/debonding
Hazardous conditions rate 2
If defect on precast or pre-stressed girder deck top is severe enough to affect load carrying capacity then girder rating should also be consistent
Deck Top

## Slide 52: Deck Top

## Slide 53: Gravel Abrasion and Edge Spalls

## Slide 55
Notes: Also affects girder rating

## Slide 56: Lateral Connection Problem Y/N
PCS (precast or pre-stressed standard)

## Slide 57
Notes: Also affects girder rating

## Slide 58: Failed Lateral Connector Pocket – HC Girder
Notes: Also affects girder rating

## Slide 59: PE Girder Lateral Connection

## Slide 61
A measure of the riding comfort at the legal speed
Influenced by the condition of the wearing surface or deck top and joints (rated separately)
Drive over at legal speeds and assess ride quality
Listen for unusual noise from traffic
Observe traffic for signs of poor rideability such as slowing down or bouncing
Smooth, no speed reduction rate 7 or more
If speed has to be reduced due to potholes, etc. - rate 4 or less
Slipperiness reduces rating
Deck Rideability

## Slide 62: Hazardous Wear Surface due to failing ACP

## Slide 63: Deck Joints
Purpose
  Provide a structural termination of individual spans
  Can be designed to prevent water and salt from leaking down onto substructure
  Protects ends of precast girders (buffer angles)
  Can be designed to span gap between spans
  Provide a smooth transition (reduces bumps)
On standard bridges all joints are considered fixed.
Not applicable to standard TT bridges

## Slide 64
Standard Bridge Types
  Buffer angles - steel angles cast into top edge at ends of girder
  Compression seal - a compressible seal held in place by steel angles
  Strip seal installed at piers of overlays
  Others - caulked saw cuts, asphaltic plug joint (Koch or Thorma-joint)
  Asphalt fiber board alone is not a joint – rate X
Unprotected girder ends is not a joint – rate X
Deck Joints

## Slide 65
Observe traffic crossing over joints
  Listen for unusual noises
  Watch for movement
Look for:
  Vertical alignment
  Corrosion
  Deteriorating concrete around anchorages
  Damage from snowplow
Indicate whether or not a significant bump by Yes or No
  If “Yes”, explain location and cause
Deck Joints

## Slide 66
Buffer angles should not be rated down because they leak
Damage from leakage rated in substructure
Slightly less than adequate but no maintenance required – rate 4 (missing section of buffer angle)
Joints requiring repair – rate 3
Joints which are a hazard to traffic - rate 2 or less
If joint is not visible:
  Rate “X” if it is known that no joint exists
  Rate “N” otherwise
  Provide explanation
Deck Joints

## Slide 67: Missing Buffer Angles – Rated 5

## Slide 68: Void under Buffer Angle – Rated 3

## Slide 70: Deck Drainage
Ability of the deck to drain and properly dispose of water from its surface
Not applicable to bridges with timber decks
Drainage system includes gutters, inlet boxes, pipes and catch basins

## Slide 71
Poor drainage
  Common cause of deck deterioration
  May be hazardous due to hydroplaning or icing
  Caused by inadequate design, construction or maintenance practices (grade, crown, debris, etc)
  May affect other superstructure components, substructure, headslopes and sideslopes
Deck Drainage

## Slide 72
Indicate whether or not the drains are plugged by Yes or No
  If no drains, note in Explanation of Condition
Check drainage system - determine if water is properly directed off deck
If there are any deficiencies in the drainage system or significant deterioration of any components - rate 4 or less
If erosion is being caused on the headslopes or sideslopes by deck drainage - rate 4 or less
If water is ponding on deck and creates a hazard for traffic - rate 2 or less
Not a factor on timber decks therefore rate X
Deck Drainage

## Slide 74: Curbs/ Medians
Raised surface at the edge of the roadway
Purpose
  Guide or redirect traffic
  Divide the bridge according to travel direction
  Anchor railing posts
Applies to concrete only - timber or steel called wheel guards

## Slide 75
Curb consists of:
  the vertical or sloped face along the edge of the roadway
  the raised horizontal surface
  the fascia or outside surface down to the deck or girder level
Curbs/ Medians

## Slide 76
Look for:
  Scaling
  Other material defects - cracks, delaminations, spalls
  Snowplow damage along inside faces
  Accident damage
  Holes exposing the voids
  Water in voids and associated freezing damage
  Whether curb lift hook pockets are filled
Estimate the amount of scaling as a percentage of the total area
  Record the percentage in the appropriate field
  Describe the extent and location in the Explanation of Condition
  Scaling is not normally a problem on gravel roads unless using calcium chloride for dust control
Curbs / Medians

## Slide 77
Note any loss of height due to excessive roadway paving or accumulation of dirt or gravel
Rate according to condition and ability to perform as designed
  Condition of concrete
  Ability to withstand and redirect traffic
  Ability to contain railing anchors in the event of a collision
Curbs with holes or exposed voids allowing water - rate 4 or less
Severe scaling (>25 mm deep) - rate 4 or less
Reduced height (>25%) due to excess gravel or overlay – rate 4 or less
Spalling or broken concrete affecting post anchorage - rate 3 or less
Curbs / Medians

## Slide 78: Curb and Post rated 3

## Slide 79
Curb and Post Rated 3

## Slide 80
Curb holes – Rated 3

## Slide 81
Curb hole rated 3

## Slide 82
Curb is rated “X” in the example
Plinth deterioration is rated under bridgerail post section on form.
SC Girder Deterioration at Plinth

## Slide 83
Curbs made out of timber or steel
Found on timber decks
Verify type, height and width
Record in nominal dimensions (typ. size is 100 x 300 or 150 x 300 but some variations)
Revise as req’ in inventory area on form
Add this information if missing
Record wheel guard block dimensions in comments area if needed
Wheel Guard

## Slide 84
Look for:
  Poor anchorage
  Material defects
  Missing or loose bolts
  Poor connections
  Mis-alignment
  Collision damage
  Snowplow damage
  Missing sections
Note any loss of height due to roadway paving or accumulation of dirt or gravel
Rate according to condition and ability to perform as designed
Minor splits/cracks rate 5
Missing/broken sections, blocks, anchors rate 4 or less
Wheel Guard

## Slide 86: Grader damage to TT Wheelguard – Rated 4 or less

## Slide 87: Bridge Rail & Posts
Considered to be safety features
Do not contribute to the strength or load carrying capacity of the bridge
Refer to Section 7.11.2 in the manual for a list of railing and post types
Verify railing and post types – correct/add in inventory area
Record coating type on rails and posts
Record number of layers of flexbeam in comments

## Slide 88
Look for:
  Material defects (corrosion, cracks)
  Collision damage
  Horizontal and vertical misalignment
  Loose connections
  Missing nuts or bolts
  Inadequate thread engaged on post anchor nuts (< 2 threads projecting)
  Broken or spalled post anchors
  Correct lap direction of flexbeam
    lapped in direction of traffic
  Includes pedestrian rails found on sidewalks
Bridge Rail & Posts

## Slide 89
Rate according to condition and not the standard of the rail, posts or coating
  Timber rail is substandard but can be rated 9 if in new condition
  Timber posts with wrong orientation
Rating for rail and posts does not include the condition of the coating – rated separately unless severe corrosion affecting rail/post
If coating on rail and posts is different, record and rate rail coating. Note post coating type and condition in Comment area
Railing with minor collision damage but still functional and has good connections rate 5
Timber with signs of rot rate 4 or less
Rail connections with missing/loose bolts, improper laps, rate 4 or less
Railing with missing sections - rate 2 or less
Bridge Rail & Posts

## Slide 90: Bridge Rail & Posts
Post anchor bolts with at least two threads above the nut rate 8 or more
Post anchor bolts that are engaged with full/flush nut (no thread projection above the nut) or <2 threads projecting above nut rate 7
Post anchor bolts with insufficient thread (negative thread projection) rate 4 or less
Post anchors that are broken or missing anchor nuts and bolts rate 3 or less

## Slide 91: Bridge Rail & Posts
For Bridgerail posts on SC Girders:
Concrete section loss that does not extend to edge of post base plate – Rate 3.
Concrete section loss extending up to or below edge of post base plate – Rate 2.
Exposed exterior stirrups within 500 mm longitudinally of bridgerail post – Rate 2.

## Slide 92
Rotted Timber rail – Rated 3

## Slide 93
Rot in top of timber rail post – Rated 4

## Slide 94
Missing bridgerail section – Rated 2

## Slide 95
Missing Rail and Posts – Rated 2

## Slide 96
New W-beam Rail – Rated 9

## Slide 97
Missing Splice Bolts – Rated 4

## Slide 98: Anchor bolts with 2 or more threads projecting above nut – Rated 9

## Slide 99: Anchor bolts with flush or < 2 threads projecting above the nut – Rated 7

## Slide 100: Anchor bolts with flush or < 2 threads projecting above the nut – Rated 7

## Slide 101: Anchor bolts - insufficient thread projection above nut – Rated 4

## Slide 102: Loose anchor bolt nuts – Rated 4

## Slide 103: Missing anchor bolt nut – Rated 3

## Slide 104: SC Girder Deterioration Affecting Post Anchorage – Post Rated 2.

## Slide 105: SC Girder Deterioration Affecting Post Anchorage – Post Rated 2

## Slide 106: Typ. TT wheelguard, TT posts, galv. rail

## Slide 107: Sidewalk
Applicable to PCS bridges
Designed to accommodate pedestrian traffic
Not normally part of the load carrying system of the bridge
If part of the load carrying system, rating & inspection procedures are similar to “Deck Top” and/or Girder”

## Slide 108
Look for:
  Smoothness, adequate traction and debris
  Accessibility for pedestrians to the sidewalk at both ends of the bridge
  Material defects
  Condition of structural members and connections
  Condition of railings (rate under bridge rail)
Hazards to pedestrian traffic (tripping, slipping, holes, loose boards, etc.) rate 2 or less
Rate according to condition and ability to perform as designed
Rail systems rated with Bridgerail
Some defects may be less serious on a sidewalk than on the bridge
Sidewalk

## Slide 110
Applies only to Standard TT bridges
The “structural” part of the deck
Strip deck usually installed on top to protect
If no wearing surface, subdeck is in contact with traffic
Consists of timber planks fastened to stringers
Often only visible to inspect at underside and ends
Verify type and revise or add as needed
  Record in Inventory area of form.
Record nominal width and thickness – normally 100 x 300mm
Subdeck

## Slide 111
Look for:
  Material defects
  Loose or broken planks
  Deflection under traffic
Estimate the percentage of the area which has defects and record value
  Decay, staining, split or broken planks
Minor stains/cracks (concrete) rate 5
Spalls or severe scaling rate 4
Rot/Decay in timber rate 4 or less
Note location in Manual – Section 7.21
Subdeck/Underside

## Slide 112
Rot/bulging in Subdeck – Rate 3 or less

## Slide 113: Rot in Subdeck Ends – Rate 4 or less

## Slide 116: Stringers
Applies only to standard TT bridges
Longitudinal beams resting on the caps and supporting the deck
The main load carrying members of the superstructure
Verify number per span or add if missing
Verify type, size (width and depth), and spacing in nominal dimensions and record in Inventory area of form
Superstructure
Stringer Detail Ratings
Stringers
(Depth (mm) : )
(Width (mm) : )
(Type : )
(No. of Stringers : )
(Spacing (mm) : )

## Slide 117: Stringers
Purpose:
  Support the deck
  Transfer loads to substructure
  Critical load carrying members
Repaired or “sistered” stringers count as one stringer (repair must be with equivalent size stringer)
Record if stringers are notched including location

## Slide 118: Stringer and Girder Numbering

## Slide 119
Look for:
  Material defects
    decay, cracks, checks, fire damage, sags, twists
  Broken or missing stringers
  Adequate bearing, proper connections and any splitting, crushing or decay in bearing area
  Collision damage or abrasion from ice or drift
  Notches at ends in bearing zone
Stringers

## Slide 120
Cracked stringers rate 3 or less
Stringers with less than 75 mm bearing on the cap rate 3 or less
Stringers with 75 -100 mm bearing on the cap rate 4
Stringers that are bowed or twisted significantly - rate 4 or less
Cracked or broken stringers which have been repaired with additional stringer(s) of equal size may be rated 5 or more
Stringers with notches at ends - rate 7 or less and note in comments area
Record number of stringers rated N, 1, 2 & 3 in Detailed Rating boxes. If number cannot be determined, record as 99
If all stringers are rated 4 or more, Detail Ratings are recorded as ”0”
Stringers

## Slide 121: Rotted subdeck & rotted/cracked timber stringer. Both rated 3 or less.

## Slide 122: Cracked Timber Stringer –Rated 3

## Slide 123: Cracked Timber Stringer – Rated 3

## Slide 124: Cracked Timber Stringer – Rated 3

## Slide 125
Notched Timber Stringers – Rate 7 or less. Cracked Stringer Rate 3

## Slide 126
Applies only to concrete girder bridges
Longitudinal beams resting on caps
The main load carrying members of the superstructure
The deck is integral with the girder
Detail ratings only on PCS
Last Complete Inspection Date
Girders
Superstructure
Girder Detail Ratings
Last Complete Inspection Date
Grouted (Y/N)
Girders
Lift or Connector Pocket
(Number Of Girders : )
Cracking (Y/N)
Spalling (Percent Area)

## Slide 127
Purpose:
  Support the deck
  Transfer loads to substructure
Two types in Standard bridges – PCS form used for both
  Channel Girders - conventionally reinforced channel girders
  Standard Prestressed – short box girders with pre-tensioned reinforcement
  Refer to BIM Reference Manual for types of girders
Girders

## Slide 128: Girders 1.1 from BIM Manual

## Slide 129: Girders
Cracks are often the first visible sign of distress or failure
Types of cracks:
  Vertical hairline cracks on precast channel girders - common not serious
  Vertical cracks in the tension zone – flexure – usually not serious unless wide
  Diagonal cracks near supports - shear or combination of shear and flexure, can be serious
  Longitudinal cracks in bottom of legs in precast girders – common, corrosion of rebar
  Wide longitudinal cracks in bottom of legs with corrosion may lead to spalling
  Longitudinal cracks in ends of prestressed girders - stresses from pre-tensioned reinforcement
  Wide longitudinal cracks with corrosion in girder undersides of prestressed girders may be from strands and is usually serious.
128

## Slide 130
Look for:
  Cracks
  Spalling on bottom of legs
  Other defects - scaling, staining, etc.
  Damaged connectors - deteriorating grout, loose or broken bolts, corrosion on bolts or connector channels
  Spalls at dowel locations
  Collision damage or abrasion from ice or drift
  Punchouts in deck
Look for excessive vibrations or deflections under traffic
  Observe whether girders with lateral connections deflect independently
Girders

## Slide 131
Indicate cracking by Yes or No
  Applies to all types except shrinkage and hairline or narrow flexural cracks
  If Yes explain - location, type, size
  Mark and date cracks
Record the percentage of spalling on the bottom of the legs
  Record 0% if none
  Explain if any
Indicate Lift or Connector Pockets Grouted
    Yes or No
  If Yes provide coment to explain
Verify total number of girders or record number per span if blank
Girders

## Slide 132
Standard reinforced channel girder rating guidelines in Section 7.15.3 –Section 7.15.3.5 and are summarized Table 7.4
Standard prestressed girder ratings in Section 7.15.4 – 7.15.4.4 and summarized in Tables 7.5, 7.6 and 7.9
  Rating guidelines for BOTH types 7.14.1 – 7.15.2.7
Ratings given are maximums - decrease as required depending on defect
  Reflect condition and functionality
Defect on curb girder only, can increase rating by one if traffic not on girder
Provide girder count for N, 1, 2 & 3 ratings
If girder ratings are 4 or above detail ratings are “0”
Girders - Rating Guide

## Slide 133: Rating Guide – Table 7.4 Standard Reinforced Girders

## Slide 134: Rating Guide - Standard Reinforced Concrete Girders

## Slide 135: Spall in AZ with <50% of bars embedded in sound concrete – Rated 2.

## Slide 136: Spall in AZ with <50% of bars embedded in sound concrete – Rated 2.

## Slide 137: Spall in AZ of curb girder with <50% of bars embedded in sound concrete – Rated 2 + 1 = 3

## Slide 138: Narrow shear crack – Rated 5

## Slide 139: Multiple narrow shear cracks – Rated 5

## Slide 140: Spall in end diaphragm extending into legs – Rated 2

## Slide 141: Spall in AZ with heavy corrosion and broken shear stirrup – Rated 2

## Slide 142: Spall in AZ with heavy corrosion and broken shear stirrup – Rated 2

## Slide 143: Spalling in AZ with heavy corrosion and deterioration of deck / girder underside – Rated 3

## Slide 144: Delamination / partial punchout at girder underside – Rated 3 or less.

## Slide 145: Full depth punchouts at girder underside – Rated 3 or less.

## Slide 146: Rating Pre-stressed Girders
Refer to Sections 7.14 to 7.14.3 for general information.
Refer to Section 7.15.4 to 7.15.4.3 for specific information.
Summarized in Tables 7.5, 7.6, and 7.9
Suggest using “3-strike” rule to determine ratings for pre-stressed girders.
Start with Table 7.9 – Exception List for common standard prestressed girder types (VS, SM, SC, SL).
  Note that crack width must be narrow – reduce by 1 if corrosion staining is present.
  If defect in field matches description in Table 7.9 then rate accordingly.
Refer to Table 7.6 – Exception List for ALL Pre-stressed Girders.
  If defect in field matches description in Table 7.4 then rate accordingly.
3. Refer to Table 7.5 – rate accordingly

## Slide 147: Rating Guide for Prestressed Girders – Table 7.9 Exception List - SL, SC, SM, VS
Crack | Rating | Description
1 | 5 | Diagonal crack on bottom of girder, not longer than 0.5 m. Crack length must be continuous and not intermittent or staggered. Crack lengths to be measured from the face of the pier cap or abutment seat and along the length of the crack (with no signs of corrosion staining).
 | 3 | Diagonal crack on bottom of girder, not longer than 0.5 m. Crack length must be continuous and not intermittent or staggered. Crack length to be measured from the face of the pier cap or abutment seat and along the length of the crack (with signs of corrosion staining).
2 | 5 | Longitudinal crack on girder underside.
3 | 5 | Longitudinal crack at lower curb fascia.
4 | 5 | Crack in poured connection at fascia over piers (RM, RD,SMC, SCC, SCM, SLC).

## Slide 148: Rating Guide Table 7.6 Exception List for ALL Prestressed Girders
Exception List - All Prestressed Girders
Crack | Rating | Description
1 | 6 | Narrow map cracks.
 | 4 | Medium, wide or any map cracking with corrosion staining.
2 | 3 | Vertical crack 50 to 100 mm from end of girders with or without signs of corrosion stains. No further rating reduction applied for presence of stains

## Slide 149: Rating Guide for Prestressed Concrete Girders – Table 7.5
Rating | Defects
4 | Hairline cracks with no staining except as noted below.
3 | All other cracks except as noted below. Corrosion stains originating from prestressed strands.
2 | Cracks with signs of corrosion in webs or bottom of boxes or flanges except as noted below. Any cracks which are growing
1 | Any cracks which are opening or closing under traffic or with slippage along the cracks.

## Slide 150: Typical Diagonal Cracks & Narrow Longitudinal Cracks – Rated 5

## Slide 151: Medium or wide longitudinal crack, no corrosion. Rated 3

## Slide 152: Wide longitudinal crack, no corrosion staining. Rated 3

## Slide 153: Wide longitudinal crack, with corrosion. Rated 2

## Slide 154: Narrow longitudinal crack with corrosion. Rated 4

## Slide 155: Narrow longitudinal crack with no corrosion. Rated 5

## Slide 156: Partial depth repair of prestressed box girder. Note location of strand inside of rebar.

## Slide 157: Minor Corrosion Spots – No Affect on Rating

## Slide 158
AT first learned of problem in 2012
6 SC girder bridges showing signs of accelerated freeze thaw deterioration on exterior girders.
Investigation revealed deterioration due to substandard aggregates in concrete mixes used in girders fabricated 2003-2007
88 SC girder bridges built in this time frame
36 of 88 bridges now showing deterioration with various degrees of severity.
16 - significant premature deterioration
20 - deterioration may soon become severe
Severe deterioration typically on exteriors especially if exposed to direct sunlight but interior girders are also affected
SC Girder Deterioration

## Slide 159
Issues include:
failure of the concrete plinth where bridgerail post anchors into exterior girder,
reduced structural capacity of the exterior girders due to loss of concrete and reinforcing steel embedment,
signs that damage to the tops of girders may soon become a concern for sites with no wearing surface.
SC Girder Deterioration

## Slide 160: SC Girder Deterioration Ratings

## Slide 161
Extensive scaling exterior girder surfaces , section loss along top and bottom corners.
No exposed stirrups or prestressing strand.
Section loss of Bridgerail post plinth.
Girder rated 3.
BR posts rated 3.
SC Girder Deterioration

## Slide 162
Section loss along top and bottom corners of exterior girder.
Girder rated 3.
Bridgerail posts rated 3.
SC Girder Deterioration

## Slide 163
Section loss along top corners and top surfaces of interior girders.
Interior girders rated 3.
SC Girder Deterioration

## Slide 164
Significant section loss all surfaces extending beneath bridgerail post baseplate.
Exposed stirrups.
Exterior girder rated 2.
Bridgerail posts rated 2.
SC Girder Deterioration

## Slide 165
Scaling of exterior face, section loss on top and bottom corners extending beneath the bridgerail post bases.
No exposed strands or stirrups.
Exterior girder rated 3.
Bridgerail posts rated 2.
SC Girder Deterioration

## Slide 166
Section loss at top corner of exterior girder that does not extend to the edge of the bridgerail post base plate.
Aggregate popouts on exterior face.
Concrete section loss of bridgerail plinth.
Girder rated 3.
Bridgerail post rated 3.
SC Girder Deterioration

## Slide 167: SC Girder Deterioration – Management Strategy

## Slide 168: Span Alignment Problems
Applies only to
  the vertical and horizontal alignment of the superstructure
No rating is required
Mis-alignments may indicate distress in the superstructure and/or substructure
Vertical (Y/N)
Horizontal (Y/N)
Superstructure
Last
Now

## Slide 169: Span Alignment Problems

## Slide 170
Look along edges of girders, curbs, railing for signs of sags, bows, movement, buckling, twisting, etc.
Look for vertical mis-alignment and uneven gaps at deck joints
Indicate vertical and horizontal alignment problem by Yes or No
If Yes, provide an explanation of the location, type, possible cause and seriousness
Span Alignment Problems

## Slide 171: Span Alignment Problem - Vertical

## Slide 172: Span Alignment Problem - Horizontal

## Slide 173
Refer to Sections 1.10.2 and
Governed by
  Structural load carrying members (girders, stringers, subdeck)
  Safety concerns rated 2 or less (e.g. missing bridgerail, severe bump, severe span alignment problem)
  Hazardous conditions rate 2 or less (e.g. ponding/icing, wide ACP cracks/ruts in wheelpath)
Bridgerail not present (rated X) but creating a hazard results in General Rating of 2
General Rating

## Slide 174: Questions?