## Slide 1: CONDITION RATING
Notes: Tips:
use an icon that best represents the concept you are presenting on. Icons are available at: alberta.ca/identity
If you don’t have a subtitle, move your name and title up to create balance with the main title

## Slide 2: Why we need a rating system
A rating system provides:
  a numerical representation of the condition of bridge elements and inspection categories.
  a uniform method for describing the condition and functionality of an element

## Slide 3: Why we need a rating system (cont’d)
The ratings can be used to:
  flag safety-related problems
  identify elements in poor condition
  assign priorities to repair, maintenance, etc
  justify budget proposals
  assign priorities to repair, maintenance, etc
  justify budget proposals
  asses the health of the system
  measure rates of deterioration to
    properly time remedial work
    identify premature failures
  monitor performance of new materials or practices
  Allow for various sorting of the numeric values
  provide insight if structure components are functioning as designed

## Slide 4: Types of ratings
Condition ratings (elements)
General ratings (summarizes governing elements condition/functionality or hazards of respective sections)
Structural Condition Rating (overall rating of the structure’s structural condition in %)
Sufficiency Rating (overall rating of structure sufficiency in %)
Load rating

## Slide 5: Rating System Features
Must rate
  the individual elements of the structure
    girders, bearings bridgerail, etc.
  the major components
    approach roads, superstructure, substructure, barrel etc.
  the overall condition of the structure
    Sufficiency and structural ratings

## Slide 6: Rating System Features
Identify and flag safety concerns
Provide measure of condition and functionality of the structure components
Identify maintenance requirements

## Slide 7: Rating System Features
Logical
Simple to understand and to use
Usable in an electronic system
  numeric
  easy to input
  low storage requirement
  sortable
Easy to use in the field
  visual - i.e., rate what you see

## Slide 8: Rating System Features
Not based on
  Maintenance budgets
  Crew or contractor availability
  Standards
Rating is a measure of:
  Condition
  Functionality

## Slide 9: Condition
Existing condition of the element taking into account any deterioration from the original new conditions.
The ability of an element to perform as originally designed
Not measured according to today's standards
Examples:
  New timber railing
  Rotten Timber cap
Functionality

## Slide 10: Rating System
9 Very Good (New)
8
7 Good
6
5 Adequate
4 Fair
3 Poor
2 Hazardous
1 Immediate Action
1
2
3
Rating Descriptions

## Slide 11: Rating Systems
  Based on a 1 to 9 numeric system
  Has special characters to denote
    elements not applicable to a specific structure (X)
    elements not sufficiently accessible for an adequate visual inspection (N)
  Measures condition and functionality of components.

## Slide 12: Rating Systems
The element’s current condition and functionality is compared to a range of defined values for
  ratings
  a condition
  what rating is intended to mean
Table 1.2 in Inspection Manual
With this course and field training, goal is for certified inspectors to be able to rate elements within "1” point.
Experience and periodic ongoing training after certification ensures consistency

## Slide 13: Rating Systems
Very Good to Good (9 to 7) range
Rating | Description | Commentary
9 | Very good | New conditions No repairs in foreseeable future
8 |  | Almost new conditions No repairs required in foreseeable future
7 | Good | Could be upgraded to new condition with very little effort Repairs not required currently or expected in near future

## Slide 14: Rating Systems
Adequate or Slightly Above or Below Adequate (6 to 4) range
Rating | Description | Commentary
6 |  | Generally good condition Functioning as designed with no signs of distress or deterioration No repairs currently required
5 | Adequate | Acceptable conditions and functioning as intended. No repairs currently required
4 | Fair | Below minimum acceptable conditions Low priority for repairs Maintenance recommendations are not required Comment and photograph are required

## Slide 15: Rating Systems
Poor - Immediate Action (3 to 1) range (comments, photos, recommendations req’)
Rating | Description | Commentary
3 | Poor | Presence of distress or deterioration Not functioning as intended Need for replacement, repair, and/or signing
2 | Hazardous | May require continued observation until work is complete High priority for replacement, repair, and/or signing
1 | Immediate Action | Danger of collapse, and/or danger to users Bridge closure, replacement, repair, and/or signing required as soon as possible

## Slide 16: Rating Systems
Special Ratings:
Rating | Description | Commentary
N | Not Accessible | Element cannot be visually inspected (e.g. snow/gravel covered or deep water)
X | Not Applicable | Element is not applicable to structure (e.g. pier elements on single span bridge, longitudinal seams on CSP culvert)

## Slide 17: Maintenance Priority
4 is low priority for repair.
  Recommendation can be made but is not required.
  If made, then usually added to list of more immediate repairs or if the bridge is to be rehabilitated.
3 is medium priority, repair before next inspection.
  Next inspection date may be on a shortened inspection cycle due to critical nature of element.
2 is high priority, repair within next 3 to 6 months.
  Normally involves a reduced inspection cycle until repaired or replaced.
1 is immediate action.
  Follow-up is required.

## Slide 18: Rating Guidelines
Rate the worst element
See enough of the element to assign a rating
Rating must be given for elements partly visible when visible area/section is 4 or less.
If an element is not visible, a rating of N is assigned. Comments are provided for all N ratings explaining why the element could not be rated (e.g. snow or gravel covered, not accessible due to deep water)
If an element that was previously rated 3 or less is rated N in a current inspection, a comment is added to indicate/alert the previous rating and date for the next inspector (e.g. “P.R. 3 on May 1, 2023)

## Slide 19: Rating Guidelines
Blank ratings are not allowed and is reason for rejection of inspection report
If an element is not applicable but is required:
  rate element X
  provide comment in Explanation of Condition
  provide maintenance recommendation

## Slide 20: Rating Guidelines
If an element is not constructed according to the original design rate 4 or less
Intended to flag rare and unusual situations that may be significant to the structure
Does not apply to minor deviations from standard practice

## Slide 21: Temporary Repairs
Intended to be in place for less than two years
Do not affect the element rating
May be difficult to determine if repair is temporary or permanent
Temporary repair may also be a Special Feature and require a condition rating (e.g. timber struts <2 years in culvert barrel)
Examples:
  flexbeam guardrail placed over damaged bridgerail
  pile bent on mudsills placed in front of rotted timber piles or caps

## Slide 22: Permanent Repairs
Intended to be in place more than two years
Consider the effect of the repair when assigning a rating
Complete replacement of element may increase rating to 9
Simple repair may restore element to an adequate condition and rating of 5
Examples:
  new timber or steel cap replacing rotted timber cap
  shotcrete repair on culvert seam
  timber or steel culvert struts in place >2 years
  timber piles repaired with steel splice

## Slide 23: Rating Actions
Comments (explanation of condition) - use ONLY approved abbreviations
Ratings of 4 need a comment and a photograph
Ratings of 3 or less need:
  A comment explaining
  photographs, sketches, and measurements as required
  an accompanying recommendation for
    maintenance including dimensions and quantities
    Monitoring (used sparingly and must be measurable)
    other appropriate action.
  Reduced inspection cycle may be warranted

## Slide 24: Rating Actions
Take appropriate immediate action for condition ratings of 2 or less for critical elements or hazardous situations.
  For AT managed structures report to the Regional Bridge Manager and Bridge Preservation Specialist including suggested action within 48 hours of inspection.
  OR
  For LRA managed structures report to the responsible road authority official including suggested action within 48 hours of inspection
  Reduce the inspection cycle
  Possible warning signs/barricades
  Possible partial closure or posted loading
  Phone authorities within 12 hours if critical element rated 1 or imminent failure

## Slide 25: Rating Actions
Recommendations for maintenance (regardless of rating) need
  a detailed explanation of the recommendation
  a photo showing damage to be repaired
  recommended repair year
  a list of required materials including dimensions and quantities.
    routine or minor maintenance
    reasonably obtainable during a Level 1 inspection

## Slide 26: General Rating
Required for all inspection categories
  approach road
  bridge superstructure or culvert barrel
  bridge substructure or culvert U/S and D/S ends
  channel or grade separation
Provided by the inspector after rating the individual elements in the category
Ratings are done in accordance with same numerical rating system used for condition rating of elements
Used to calculate
  Structural Condition Rating
  Sufficiency Rating

## Slide 27: General Rating
Is a reflection of critical or hazardous element ratings in the category
BUT
Is not the average of the ratings of the individual elements
Must consider the condition of key elements and their impact on the structural integrity and safety of the bridge
  load carrying members have greater influence than non-load-carrying members
  hazardous situations may have greater influence than load carrying elements
General rating cannot be higher than lowest critical or hazardous rating
General rating could be lower than lowest critical rating
  e.g., Girders rated 3, but ponding on deck causing hazardous situation and Deck Drainage rated 2. Superstructure General Rating = 2

## Slide 28: General Rating
Examples:
Timber cap or pile rated 3 would result in a General Rating of 3 for the Substructure.
Curb rated 3 would not impact General Rating of Superstructure but Curb rated 2 due to hazard (severe loss of support under BR post) would.
Paint/Coating rated 2 not considered hazardous and no affect on Gen Rating
Refer to Section 1.10 in the BIM Manual, and at end of each Manual Section for additional guidance in assigning General Ratings.

## Slide 29: Structural Conditions Rating
A measure of the structural condition of the entire structure
Single numerical value expressed in %
For bridges:
  The sum of the Superstructure and Substructure General Condition Ratings as a percent of the maximum possible “brand new” ratings
  For Culverts:
  The Barrel General Condition Rating as a percent of the “as new” rating

## Slide 30: Sufficiency Rating
The sufficiency rating is a single numerical value expressed in %
Indicates the adequacy of a structure relative to the acceptable standard of a new structure at the same location

## Slide 31: Sufficiency Rating - Bridges
Calculated automatically by the system from inspection and inventory data then printed on the last page of the form.
Uses 4 major impact categories
  Structural Condition
  Load Carrying Capacity (strength)
  Operational and Safety
  Traffic Reduction Factor
Major categories are further divided into a total of 10 categories.
Categories weighted in accordance with their relative importance.

## Slide 32
Sufficiency Rating Calculator | 
Bridges (figure 12.1) | 
A. Structural Conditions (35%) | Superstructure (20%)
 | Substructure (15%)
B. Strength (20%) | Load Rating (20%)
C. Operational & Safety (45%) | Approach Road (12%)
 | Bridge Width (10%)
 | Vertical Clearance (8%)
 | Channel Adequacy (10%)
 | Safety Features (5%)
D. Traffic Reduction Factor (15%) | Traffic Count (5%)
 | Detour Length (10%)
Sufficiency Rating = A + B + C - D | 

## Slide 33: Sufficiency Rating - Culverts
Calculated automatically by the system from inspection and inventory data then printed on the last page of the form.
Uses 3 major impact categories
  Structural Condition
  Operational Features
  Reduction Factor
Major categories are further divided into a total of 10 categories.
Categories weighted in accordance with their relative importance.

## Slide 34
Sufficiency Rating Calculator | 
Bridges (figure 14.1) | 
A. Structural Conditions (55%) | Upstream End (7.5%)
 | Barrel Section (40%)
 | Downstream End (7.5%)
B. Operational Features (45%) | Approach Road (15%)
 | Channel Section (5%)
 | Waterway Adequacy (25%)
C. Traffic Reduction Factors (15%) | Traffic Count (5%)
 | Detour Length (5%)
 | Vertical Clearance (5%)
 | Environmental (10%)
Sufficiency Rating = A + B - C | 

## Slide 35: Sufficiency Rating Description
Ranges from 0% to 100 %
100% represents a bridge that is in excellent condition and provides the best possible level of service.
50% represents a bridge that is in adequate condition and provides an acceptable level of service.
Lower ratings indicate a bridge that is in poor condition and/or provides a below minimum level of service.
Lower ratings also indicate need for replacement, rehabilitation or maintenance.

## Slide 36: Sufficiency Rating Uses
Provides a rational basis for bridge management.
Evaluates the present adequacy to serve public needs.
Identifies structures with deficiencies that can be corrected at minimum cost to provide acceptable levels of service.
Provides data to evaluate the cost of upgrading a structure to provide an acceptable level of service.

## Slide 37: Sufficiency Rating Cautions
Should not be used as the only basis for bridge management decisions.
Does not include or identify:
  cost/benefit analysis
  social factors
  economic factors
  environmental factors
  alternatives
  optimal solutions
  timing constraints
  budgetary constraints

## Slide 38: Structural Condition & Sufficiency Rating
Refer to Chapter 12 for Bridge Structural Condition and Sufficiency Rating information.
Refer to Chapter 14 for Culvert Structural Condition and Sufficiency Rating information

## Slide 39: Questions?