## Slide 1: INSPECTION OF TRUSSES

## Slide 2: Truss Members & Elements
Bottom Chord
Top Chord
Portal Bracing
Vertical
Batter Post
Diagonal
Top Chord Bracing
Sway Bracing
Floor Beam
Lower Chord Bracing
Stringer
Sway Strut
Top Chord Bracing Strut

## Slide 3: Level II Truss Inspection
Trusses for Alberta Highways
Bridge system has about 340 sites with 470 truss spans
Majority of these trusses were fabricated between 1920 & 1930
Most of the spans are now on secondary highways and local roads
Approximately 55 truss spans remain in active use on primary highways
Some structures have been used at more than one crossing
Level II Truss inspection started in the early 1970’s
Second round of U/T inspection in 1983 revealed numerous cracked members

## Slide 4: Level II Truss Inspection
Frequency of Inspection
Provincial highways 4 – 5 years
Local roads 6 years
Special monitoring – varies depending on truss condition, age, and traffic volumes.

## Slide 5: Level II Truss Inspection
Preparation for Inspection
Check previous reports
Obtain inspection forms
Hire ND inspection company
Equipment for U/T
  Ultrasonic testing machine with 60° and 70 probes
  Coupling fluid
  Spare batteries and charging unit
  Extra probe and leads

## Slide 6: Level II Truss Inspection
Preparation for Inspection
Submit traffic safety and fall protection plans and obtain approval
Access equipment:
  Lift truck
  Snooper truck
Inspection tools
Personal safety attire

## Slide 7: Truss Inspection
Span Numbers
1
2
3
4
L0
L0
L1
L6
L2
L3
L4
L5
L0
L1
L2
L3
L4
L5
L6
L7
L8
U1
U2
U3
U4
U5
U1
U2
U3
U4
U5
U6
U7
N

## Slide 8: Truss Member Notation
U1
L0
L1
L2
L3
L4
L5
L6
U2
U3
U4
U5
Flow
N

## Slide 9: Top Chord Bracing
U5E
U5W
U4W
U4E
U3W
U2E
U3E
U2W
U1W
U1E
East
U/S
Portal
Portal

## Slide 10: Lower Chord Bracing
L0E
L0W
L1W
L1E
L2E
L2W
L3W
L3E
L4W
L4E
L5E
L5W
L6W
L6E
East
U/S
Floor Beam
Floor Beam
Floor Beam
Floor Beam
Floor Beam
Floor Beam
Floor Beam

## Slide 11: Level II Truss Inspection
Visual Inspection
Check all members and connections for:
  Cracks
  Missing or loose bolts
  Welds
  Scabs, delamination, gouges and elongated holes
  Note any strain indication
  Note any collision damage
  High water damage on bottom chord and bottom laterals

## Slide 12: Level II Truss Inspection
Visual Inspection
Check all members and connections for:
  Sags and buckling characteristics
  Measure and report distortion
  Floor beam copes
  Report on extent of corrosion, pitting and section loss
  Measure and report any top chord sweep for pony trusses
Identify member/s requiring replacement

## Slide 13: Level II Truss Inspection
Visual Inspection
Check posted and actual vertical clearance for through trusses
Report condition of deck elements
Check bearings
Check railing

## Slide 14: Level II Truss Inspection
Ultrasonic Inspection
L0
L1
L2
L3
L4
L5
L6
U1
U2
U3
U4
U5
m1
m2
m3
m4
m5

## Slide 15: Level II Truss Inspection
Ultrasonic Inspection
L0
L1
L2
L3
L4
L5
L6
U1
U2
U3
U4
U5
m1
m2
m3
m4
m5

## Slide 16: Level II Truss Inspection
Ultrasonic Inspection
Report any rough holes
Mark any member which has a crack
Report all the findings on the U/T forms
Try to determine the cause of cracking

## Slide 17: Level II Truss Inspection
Photographs
Take overall photograph of the entire bridge.
Take photographs to show condition of:
  Deck, curbs, wheel guards
  Bridgerail, bearings
  Overall condition of paint
  Typical underside
  General condition of substructure
  Specific problems

## Slide 18: Level II Truss Inspection
Looking East
D/S

## Slide 19: Level II Truss Inspection
Dirty strip deck
with broken &
worn planks

## Slide 20: Level II Truss Inspection
Damaged
wheel guard
at SE corner

## Slide 21: Level II Truss Inspection
Typical U/S

## Slide 22: Level II Truss Inspection
Sp. 1- Pier #2 bearing
over expanded
by 125 mm &
bent anchor bolt

## Slide 23: Level II Truss Inspection
Abut. #1 bearing
over expanded
by 60 mm,
twisted 25 mm
and broken anchor bolt

## Slide 24: Level II Truss Inspection
South abut. bearings
are over expanded,
neoprene pads are
at the edges of
masonry plates.
Trusses are against
the backwall.

## Slide 25: Level II Truss Inspection
Lattice rail
damaged at L1S

## Slide 26: Level II Truss Inspection
Bent bottom chord, L7-L8W (U/S)

## Slide 27: Level II Truss Inspection
Erosion at West
abutment

## Slide 28: Level II Truss Inspection
Timber planks
missing at South
pier

## Slide 29: Level II Truss Inspection
Broken stringer
second from U/S
East approach

## Slide 30: Level II Truss Inspection
Top chord
bracing U3S-U4N
has broken
gusset at U3S

## Slide 31: Level II Truss Inspection
Modified sway brace connections
were welded to the verticals, and
then the welds were removed
and bolt fasteners installed.

## Slide 32: Level II Truss Inspection
Span 2, top chord
bracing U9N-U8S
have slotted holes
at U9N

## Slide 33: Level II Truss Inspection
Span 2, at U9N,
there are six
loose bolts

## Slide 34: Level II Truss Inspection
Outside top chord U4U5N is
missing 3 bolts

## Slide 35: Level II Truss Inspection
Portal U7EU7W
is damaged with
two 50 mm
notches and
broken
clearance sign.

## Slide 36: Level II Truss Inspection
Bottom sway
bracing L1S-L2N
is cracked at L1S.
Note corrosion
section loss.

## Slide 37: Level II Truss Inspection
All verticals have plug welds at
original sway brace bolt location.

## Slide 38: Level II Truss Inspection
Vertical U4-L4N at m5 strut
connection is buckled
and has notches

## Slide 39: Level II Truss Inspection
At U5N, bevel
faying fit is
torched. Reduced
edge distance

## Slide 40
MEMBER
MEMBER
L0 - U1
U1 - U2
U2 - U3
U3 - U4
U4 - U5
U5 - L6
U1 - L1
U2 - L2
U3 - L3
U4 - L4
U5 - L5
BRIDGE NAME: -------------------------------------------------------------------- SPAN NO. -------------- OF ---------- DATE: --------------------------- FILE: ----------------
TRUSS IDENT: A---------------------- 6 PANEL TRUSS ----------------------- FT./M. SPAN, INSPECTOR:---------------------------------------------- PAGE: 1
VERTICALS
ULTRASONIC INS.
TRUSS INSPECTION
TOP CHORD
A END
B END
A END
No Crack
Crack beyond
Rivet Head
Crack under
Rivet Head
Acceptable
Member
Reject
Member
OTHER ITEMS
B END
No Crack
Crack beyond
Rivet Head
Crack under
Rivet Head
L0 L1 L2 L3 L4 L5 L6
U1 U2 U3 U4 U5
m1
m2
Exp. Fix
Fix Exp.
DIRECTION
TRUSS
m3
m4
m5
East
U/S
Edmonton
City of Champions
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
Inward dent–20 x 200mm at L2
Welded, U/T done – no crack

## Slide 41
East
U/S
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
75mm dent and 12mm crack at L2
bullet hole near middle at inside flange

## Slide 42
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
East
U/S
E
W
E
W
E
W
E
W
E
W
W
E
W
E
75 x 200mm dent near L4

## Slide 43
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
W
E
W
E
E
W
E
W
E
W
E
W
East
U/S
20mm notch at C/L. Overall bow of 15mm.

## Slide 44
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
E
W
E
W
E
W
E
W
E
W
E
W
W
E
W
E
W
E
W
E
W
E
W
E
East
U/S
3mm section loss at horiz. gusset

## Slide 45
Whitemud Ck
2
4
Yy-mm-dd
xxxxx
75-3
90’
J. Doe
East
U/S
overall bow of 30mm

## Slide 46: Where to Find Cracks in Trusses?
Damaged members.
Tension members
Rough holes
Welds.
Members with stress reversal

## Slide 47: Truss Member Fatigue Crack
L2
L1
L0
L2
L3
L4
L5
L6
U1
U2
U3
U4
U5

## Slide 48: Questions?