## Slide 1: DECK JOINTS & BEARINGS

## Slide 2: Deck Joints (7.7 in Manual)
Purpose is to:
  bridge the gap between spans
  protect the ends of the girders
  allow for expansion, contraction and rotational movement
  prevent water and salt from leakage
Most important features are:
  watertightness
  proper anchorage
Can be fixed or expansion
  fixed are for rotational movement only
  expansion accommodates translation in addition to rotation
  located over fixed or expansion bearings

## Slide 3
Several types of joints used on Alberta bridges:
Buffer angles
Waterstops
Compression Seals
Sliding Plates
Open Finger Plates
Closed Finger Plates with Troughs
Modular Joint
Gland Joints
  Open
  Cover plated / armored
Thermoplastic Polymer Modified Asphalt
Deck Joint Sealants
Other Patented Devices/Processes
  Fel Span
  Interspan
  Jeene
Deck Joints
https://www.alberta.ca/assets/documents/trans-bridge-deck-joints-drawings.pdf
Notes: Modular joints now added: Modular expansion joints are used when the movements of a bridge exceed the capacity of a single gap joint or a finger type joint. The total movement of the bridge deck is divided among a number of individual gaps, or cells, which are created by horizontal surface beams. The individual gaps are sealed by watertight elastomeric profiles, and surface beam movements are regulated by an elastic control system.

## Slide 4: Deck Joints

## Slide 5: Deck Joints
Closed Finger Plates
Gland

## Slide 6: Buffer Angles for Fixed or Minor Expansion

## Slide 7: Individual Buffer Angles on Standard Girders

## Slide 8: Sliding Plate Expansion Joint

## Slide 9: Armored Gland Joint

## Slide 10: Armored Gland Joint

## Slide 11: Finger Plate Joint

## Slide 12: Finger Plate Joint Welds

## Slide 13: Strip Seal Joint

## Slide 14: Strip Seal Joint

## Slide 15: Strip Seal Joint with Plow Guards

## Slide 16: Gland Cross-Section

## Slide 17: “Honel” Gland Joint with Bolted Compression Connection

## Slide 18: “Modular Joint

## Slide 19: “Wabocrete” Joint

## Slide 20: Placing Wabocrete Two Component Elastomeric Material

## Slide 21: Completed Installation

## Slide 22: “Koch” Joint with Elastomeric Material

## Slide 23: Completed Koch Joint

## Slide 24: Waterstop Joint

## Slide 25: “Jeene” Joint Polymer Hot Pour

## Slide 26: RCS Dow Corning Epoxy Joint

## Slide 27: “Interspan” Joint

## Slide 28
27
Check for:
Watertightness of sealed joints
    loose or torn seals
    leakage or stains
Freedom of movement
Horizontal alignment
    evenness of gap
    fingers in alignment
Vertical alignment
    joint aligned with deck
    both sides of joint in alignment
Corrosion
Deteriorating concrete around anchorages, incomplete grout
Loose or missing bolts, cover plates or curb plates
Gouged, torn, cracked or broken
    extrusions
    angles
    plates
    fingers
    welds
Problems and Inspection Considerations

## Slide 29
Observe traffic passing over joints
  listen for unusual noises and watch for movement of the joint
Check drainage system
  plugging of joint opening, troughs and downpipes with debris
  corrosion / perforations
  cracks, breaks or tears in any component
  Integrity of attachments and connections
    loose or missing bolts
    cracked or broken welds
    loose or open connections
  Check for:
    signs of ponding on the deck
    staining or deterioration on the deck, curbs, girders and substructure
    erosion below downpipe
Problems and Inspection Considerations

## Slide 30: Hole in Gland Joint

## Slide 31: Replace Joint Seal

## Slide 32: Testing for Watertightness

## Slide 33: Missing Plow Guards and Spalled Paving Lip

## Slide 34: Finger Plate Joint with Broken/Lifted Fingers Welds

## Slide 35: Finger Plate Joint with Broken/Missing Fingers

## Slide 36: Finger Plate Joint with no Remaining Expansion

## Slide 37: Armored Gland Joint - Missing Bolts

## Slide 38: Loose Buffer Angles

## Slide 39: Wabo-crete Joint with De-bonded Material and Exposed Bars

## Slide 40: Inspection Form and Rating
Record temperature
Verify joint type
Verify joint function
  fixed
  expansion
Measure and record average gap width in millimeters for each joint

## Slide 41
Rate according to existing condition and functionality
Includes condition and functionality of drainage system
Leakage of sealed joints is reflected in both the deck joint rating and the deck drainage rating
Defects in open joints with plumbing features are also reflected in both the deck joint rating and the deck drainage rating
Leakage problems with open joints without plumbing are rated under deck drainage only
Curb cover plates are rated with the deck joint and not the curb rating
Deck Joint Inspection and Rating

## Slide 42: Deck Joint Inspection and Rating
Joints that are not fully free to move - Rate 4 or less
Joints designed to be watertight joints which allow leakage of water onto girders, bearings or substructure - Rate 4 or less
Open (non-watertight) joints should not be down rated because of leakage
Joint defects causing problems with structure (e.g. frozen bearings causing pier cap delams) - Rate 3 or less
Joints which are a hazard to traffic - Rate 2 or less

## Slide 43
Bearings must transfer loads from the superstructure to substructure.
Bearings accommodate movement caused by temperature changes, deflection, earth pressures, etc.
Bridge bearings are generally classified as fixed or expansion type and located under corresponding joints.
Fixed bearings allow rotation but no vertical or horizontal movement.
Expansion bearings allow both rotation and longitudinal movement of the superstructure. Expansion bearings sometimes also permit transverse movement.
Bearings (7.20)

## Slide 44: Bearings
There are usually three distinct components in a bearing:
Sole plate - Steel plate welded, bolted, riveted or cast to bottom of girders
Masonry plate - Similar to sole plate except located on top of substructure element and usually anchored by bolts into concrete
Bearing - Assembly between sole plate and masonry plate that permits movement of the bridge

## Slide 45: Bearings
The common types of bearings used on Alberta bridges are:
Elastomeric pads
  Usually neoprene – newer are reinforced with steel shims, older are plain/un-reinforced
  Often include stainless steel and teflon for expansion of longer span girders
Rockers
  Large steel “pie-shaped” bearings designed for large movements
Rocker Plates
  Steel plate with cylindrical side - accommodate rotation only–fixed so no thermal movement
Pot
  Elastomeric pad confined by heavy steel ring & loaded vertically by cover component. Can allow movement in one or more directions, be fixed, and be designed to resist uplift.

## Slide 46: Bearings cont’d.
The common types of bearings used on Alberta bridges (continued):
5. Roller/Roller Nest
  Cylindrical steel bearings either in the form of a single roller or in a group (nest). Rollers allow rotation and horizontal movement in one direction.
6. Neoprene Strip Bearing
  Fixed bearing used under short span standard girders not requiring movement
7. Steel Sliding Plate w/Self Lubricating Bronze Plate
  Steel plates with bronze plate between – used primarily under Type O girders (1955-19650
  Problems with freezing and inducing stresses to substructure

## Slide 47: Bearings cont’d.
The common types of bearings used on Alberta bridges (continued):
8. Spherical bearings
  Made of spherical machined steel plates that nest together to allow rotation and may have an allowance for horizontal movement
10. Sliding Plates
  steel sliding expansion plates commonly used under pony trusses – simple and no problems
11. Disc/Disc and Dome
  disc bearings (round, confined polyurethane pad)
12. Others
  Rotation Pins - allows truss rotation of fixed bearings
  Pinned – fixed stacked plates (opposite of sliding plates)
  Pedestal

## Slide 48: Bearings
ELASTOMERIC PAD
POT BEARING

## Slide 49: Bearings
48
ROCKER BEARING
ROLLER BEARING

## Slide 50: Bearings
SPHERICAL BEARING
BEARING WITH SLIDING SURFACE

## Slide 51: Elastomeric Bearing Showing Pintel, Anchor, Bolts, Sole and Masonry Plates (before grouting)

## Slide 52: Reinforced Neoprene Expansion Bearing with Teflon & Stainless Steel

## Slide 53: Reinforced Neoprene Bearing without Teflon & Stainless Steel

## Slide 54: Pot Bearing - Expansion

## Slide 55: Multi Pot Bearings - Expansion

## Slide 56: Rocker Bearing Under Steel Girder

## Slide 57: Plate Rocker Bearing Under Truss

## Slide 58: Rocker & Plate Rocker Bearings

## Slide 59: Single Roller Bearing Under Concrete Girder

## Slide 60: Roller Nest Bearing Under Concrete Girder

## Slide 61: Roller Nest Bearing Under Truss

## Slide 62: Neoprene Strip Bearing Under Std. Girders

## Slide 63: Sliding Plate with Self-Lubricating Bronze Plate (Type PO Girders)

## Slide 64: Rotation Pin (Fixed) Bearing Under Truss

## Slide 65: Rotation Pin (Fixed) Bearing Under Acrow

## Slide 66: Sliding Plate Under Truss

## Slide 67: Steel Plate Pinned (Fixed) Bearing

## Slide 68: Bearings
Problems and Inspection Considerations
Dirt or debris
  may inhibit movement
  promotes corrosion
Corrosion
  “frozen” bearing (“Type O” bearings most affected)
  deterioration of bearing
    especially under leaking joints

## Slide 69: Bearings
Problems and Inspection Considerations
Loose or missing connections, cracked or broken welds
Loss of bearing contact or uneven contact
  rollers moved off masonry or sole plates
  neoprene pads creeping out of position
  can overstress steel or concrete members

## Slide 70: Bearings
Problems and Inspection Considerations
Wear
Rocker alignment
  overextension
  should be approximately vertical at 0° Celsius
Failure of elastomer
  splitting, cracks, squeezing out, bulging
  separation of the elastomer at reinforcing plates

## Slide 71: Bearings
Problems and Inspection Considerations
Anchor bolts
  corrosion (strike with hammer)
  bent
  surrounding concrete cracked
  nuts not properly secured (jam nut), nuts missing
  binding on shoe plate or bearing device

## Slide 72: Bearings
Problems and Inspection Considerations
Indications of a non-functioning bearing
  cracks in the bearing area of the substructure or superstructure
  uneven gaps at expansion joints
    bump at joint
    variable gap in same joint
    jammed joint
    joint gap too wide
  misalignment of superstructure at joint
  unusual noise or movement under traffic

## Slide 73: Bearings
Problems and Inspection Considerations
Deterioration caused by leaking deck joints should be noted in Explanation of Condition.
- Deck drainage also gets down-rated
- If joint above was designed to be watertight then joint also gets down rated
Cracks, delaminations or spalls in concrete abutment and pier’s caps / seats / corbels emanating from bearing components should be noted and comments on reduced bearing functionality should be provided.

## Slide 74: Bearings
Inspection Form and Rating
Record temperature
Record or verify bearing types and locations:
  expansion
  Fixed
Record if coating intact and functioning to protect bearing from corrosion
Record or verify whether the bearing is functioning as designed
  proper bearing
  proper movement

## Slide 75: Bearings
Inspection Form and Rating
Bearings functioning properly and in good condition but have inadequate coating
  Rate 7 or 8
Bearings require resetting
  Rate 4 or less
Bearing movement inhibited by dirt, debris or corrosion (frozen)
  Rate 4 or less
Concrete elements under bearings with wide cracks or visual signs of damage (not accessible for sounding)
  Rate 3 or less
Pin and Hanger bearings with cracked hanger
  Rate 2 or less
  Corrosion, frozen pins, missing windlocks – rate 3 or less

## Slide 76: Displaced Neoprene Pad

## Slide 77: Displaced Neoprene Pad - Over Keepers

## Slide 78: Torn Neoprene Pad Bearing

## Slide 79: Pot Bearing – Failed Keeper Plate

## Slide 80: Pot Bearing – Cracked

## Slide 81: Extended Rocker Bearing (rating dependent on temp)

## Slide 82: Failed Rocker/ Roller Bearing

## Slide 83: Displaced Roller Nest

## Slide 84: Pinned/Fixed Bearing with Corrosion & Failed Grout Pad

## Slide 85: Pinned Bearing with Sheared Anchor Bolt

## Slide 86: Sliding Plate Bearing Unsupported

## Slide 87: Sliding Plate Bearing Unsupported

## Slide 88: Type PO Girder Bearings
Performance issues related to steel sliding plate bearings with self-lubricating bronze plates.
Primarily found under Type “PO” girders between 1955 and 1965, and detailed on Standard Drawing S-701.
Failed bearing at BF 1153 Hwy. 22 over Oldman River discovered during Level 1 BIM inspection. Near catastrophic and led to BIM Bulletin 3 Jan. 2016

## Slide 89: Failed Sliding Plate with Self-Lubricating Bronze Plate Bearing

## Slide 90: Failed Sliding Plate with Self-Lubricating Bronze Plate Bearing

## Slide 91: Failed Sliding Plate with Self-Lubricating Bronze Plate Bearing

## Slide 92: Failed Self-Lubricating Bearing Replaced with Neoprene Pad Bearings

## Slide 93: Questions?