## Slide 1: SIGN STRUCTURE INSPECTION & RATING

## Slide 2: Introduction
Definition – sign or multiple signs with area >4 m2
Signing for Interchanges – normally have associated BF #
Naming Convention
  Site file number 75760
  Visual identifiers
    Z = sign structure
    W, E, N, or S = direction of approach
  Structure number 2 = 2nd structure (travelling north)
  Example 75760-ZN-2
  Numbering convention – 1st sign come to (farthest away) is #1
  If another sign is added all signs in that direction get re-numbered

## Slide 3: Introduction
Refer to Chapter 15 in BIM Manual
Other sections on form are rated consistent with other structures (e.g. Approach Road and Approach Guardrail)
Rating and Recording requirements same as for other structures
Measure and record vertical clearance if possible
Minimum acceptable VC on provincial highways is 6m**. If VC on form is <6m – or if inspector suspects VS is not accurate recommend L2 VC

## Slide 4: Utilities
Verify and update
Chapter 4 BIM Manual
Note and record location within 200 m
Many structures have lights
Others have hi-vis sign resolution
Report hazards with utilities immediately (LRN 12/48 hrs)
Inventory Data

## Slide 5: Approach Road / Safety Features
Horizontal and vertical alignment
  Rate same as Chapter 6 of BIM
Traffic Safety Features
  Advance warning light, flashing lights, barriers, signs, impact attenuators
  Rate function and condition – refer to 15.5.2
Guardrail (rate barriers as TSF)
  Inspect and rate according to 15.5.3 – 20 m each direction from sign
  Record length and termination Type
  Meets standard Yes / No (if “No” explain why)
    Current preferred system is flexible HTCB
    Refer to 15.5.3.1 for other system types

## Slide 6: Substructure
Substructure accommodates
  Dead Load of sign structure
  Live Loads such as wind, collision

## Slide 7: Substructure (Cont’d)
Pedestal
  Provides base for column attachment
  Record number and type (usually concrete, maybe steel)
  Measure and record offset from EOP to c/l of pedestal
    record min. if more than one present and record offset in comment area if other
  Comment if top of pedestal <850 mm above ground
  Defects affecting load carrying capacity rate 3 or less
  Check for scaling, spalling or corrosion (light scaling not serious)

## Slide 8: Substructure (Cont’d)
Column
  Carries bridge loads to pedestal
  Confirm Steel Ident Tag on column matches form
  Generally steel (HSS); susceptible to deicing salts and vehicle damage
  Check vertical alignment
  Check weld stiffeners at bottom of columns (if present)
  Check for collision damage
  Check surface condition, welds, connections, etc.
  Heavy corrosion or pitting rate 4 or less
  Cracks rate 3 or less

## Slide 9: Substructure (Cont’d)
Connection / Bearings
  refers to column-to-pedestal connection
  corrosion resulting in loss of section rate 4 or less
  missing or loose nuts, rate 4 or less (suggest missing nuts =3 unless lock nut)
  check all welds for cracks – if present rate 3 or less
Coating
  refers to coating on column (typically galv) and pedestal (typically none)
  top coat deteriorated, primer intact – or no corrosion but touch up req’ rate 5
  pitting and / or loss of section (5%) rate 4 or less
  pitting and / or loss of section (>10%) rate 3 or less

## Slide 10: Superstructure
Refers to portion attached to columns and spanning the road

## Slide 11: Superstructure (Cont’d)
Special Features
  Refers to temporary or permanent
  Not items identified as Traffic Safety Features
  Typical examples
    high load indicators,
    special lighting,
    hazard signing or flashers,
    column brace,
    wind deflectors

## Slide 12: Superstructure (Cont’d)
Truss Members
  rating details Chapter 7.16 of BIM Manual
    bottom chord
    diagonals
    verticals
    connections
  check lower members for collision damage
  tension members look for fatigue cracks
  defects affecting load carrying capacity rate 4 or less
  corrosion or pitting resulting in section loss rate 4 or less
  cracks rate 3 or less

## Slide 13: Superstructure (Cont’d)
Access platform (present on older signs)
  platform and rail used for maintenance (signs and lights) – laid flat when not used
  not for use during routine Level I from ground with binoculars
  Check connections
  high load damage
Coating
  rating same as 15.6.5 Substructure
Span alignment problems
  check for bows, sags, bow, buckling, twists, other signs of distress
  alignment between columns is level

## Slide 14: Signs
Refers to signs on the superstructure
Includes variable message boards
Should be clear, clean and readable

## Slide 15
Record type of sign (wood or metal)
Digital variable message boards
Sign Board
  Over traffic so defects can be serious
  damage from wind, high load, etc.
  fasteners, and connections
  coating damage or deterioration
  lighting
Coating
  Usually hi-vis reflective with lighting
  Diamond grade without lighting
  Damage/difficult to read rate 4 or less
  Broken lights, loose cords 4 or less
Connections
  loose or missing bolts
  rate 4 or less
Signs (Cont’d)

## Slide 16: General Ratings
Approach Road / Safety Features
  Horizontal and Vertical alignment
  Safety concerns
Substructure
  Pedestal, Column and Connection ratings
Superstructure
  Load carrying elements
  Safety concerns
Sign
  Sign board, Connections, Coating, Illumination

## Slide 17: Sign Structure Maintenance

## Slide 18: Sign Structure Maintenance Table 11.1

## Slide 19: SIGN STRUCTURE TYPES 15.7.2

## Slide 20: COR10

## Slide 21: Tube - Double Leg

## Slide 22: Tube - Cantilever

## Slide 23: Space Truss – Double Leg

## Slide 24: Space Truss – Cantilever

## Slide 25: Truss – Double Leg

## Slide 26: Truss – Cantilever

## Slide 27: Variable Message Board – Truss Cantilever

## Slide 28: Variable Message Board – Tube Cantilever

## Slide 29: Variable Message Board – Vermac Lollipop

## Slide 30: SIGN STRUCTURE SPECIAL FEATURES

## Slide 31: Wind Deflectors on COR10

## Slide 32: Wind Deflectors https://www.youtube.com/watch?v=GmEgH6jAV2k

## Slide 33: Column Support Arm

## Slide 34: SIGN STRUCTURE TYPICAL DEFECTS

## Slide 35: Crack in Top Chord

## Slide 36: Crack in Top Chord

## Slide 37: Crack in Access Platform Support

## Slide 38: Crack in Vertical at Bolt Hole

## Slide 39: Crack in Diagonal

## Slide 40: Crack in Column of COR10

## Slide 41: Cracks in Column Joint Welds of COR10

## Slide 42: Crack in Column Plate Weld

## Slide 43: Crack in Column Plate Weld

## Slide 44: Crack in Bottom Chord

## Slide 45: Crack in Bottom Chord – Stop Drilled

## Slide 46: Crack in Bottom Chord – Weld Repair

## Slide 47: Crack in Bottom Chord – Metallized

## Slide 48: Crack in Bottom Chord – Steel Sleeve

## Slide 49: Buried Pedestal

## Slide 50: Loose Anchor Bolt Nuts

## Slide 51: Missing Anchor Bolt Nuts

## Slide 52: Loose Bolt

## Slide 53: Loose/Displaced Sign Clip

## Slide 54: Loose Top Chord Connection Bolts

## Slide 55: Column Perforations

## Slide 56: Collision Damage

## Slide 57: Collision Damage

## Slide 58: Collision Damage

## Slide 59: Questions?