## Slide 1: STRUCTURAL CONSIDERATIONS FOR BRIDGES

## Slide 2: Introduction
Bridge members must be able to carry loads applied to them.
Forces resisted by bridge members:
  Axial forces
  Bending forces
  Shear forces
  Torsional forces
This presentation considers:
  How bridge members are stressed by loads
  How bridge materials resist stress
  How bridges accommodate thermal movements

## Slide 3: Force
Fy
F (Force)
Fx
Fz
Notes: Resultant force comes from it’s components (directions). Vice versa.

## Slide 4: Stress
What is a stress?
  Loads cause stresses
  Stresses are the internal force effects
How to calculate stress?
200
100
40000 N
Stress = Force/Area
= 40000/200x100
= 2MPa

## Slide 5: Strain
It is described as the amount of deformation.
It denotes the ratio of materials deformed dimension to its original dimension.
L
ΔL
Strain = ΔL / L

## Slide 6: Deformation & Modulus of Elasticity
Elastic Deformation – reversible distortion of a material.
Plastic Deformation – the irreversible distortion of a material.
Modulus of Elasticity (E) = Stress/Strain

## Slide 7: Response to Loading
Forces resisted by bridge members:
  Axial forces
  Bending forces
  Shear forces
  Torsional forces

## Slide 8: Response Loading
Rigid Body
A rigid body does not deform under load.
Equilibrium
When a particle is at rest or moves with constant velocity.
  ∑V = 0
  ∑H = 0
  ∑M = 0
Notes: Newton’s third law. Action has equal reaction

## Slide 9: Types of Applied Stresses
STRESS
PLANE
FORCE
FORCE
Tensile Stress
Notes: Skinny
Hanger external shear stirrup

## Slide 10: Types of Applies Stress
STRESS
PLANE
FORCE
FORCE
Compressive Stress
Notes: Fat
Pier column

## Slide 11: Types of Applied Stresses
Positive Moment
C
T
N.A
Tension (T)
Compression (C)
Neutral Axis (N.A)
Notes: midpsan

## Slide 12: Types of Applied Stresses
C
T
N.A
Tension (T)
Compression (C)
N.A
Negative Moment
Notes: Like over a pier

## Slide 13: Bending Stress
C
fb
Bending Stress
fb = Mc/I

## Slide 14: Types of Applied Stress
Shear Stress
FORCE
STRESS
PLANE

## Slide 15: Beams – Horizontal Shear Stress
HORIZONTAL
SHEARING PLANE
SHEAR STRESSES
DIAGONAL TENSILE STRESS
Notes: Why we have studs or dowels from girders to deck
Why we have shear stirrup in concrete (Tension)

## Slide 16: Torsional Forces
Notes: Braced girders being pulled by adjacent girder. More for skewed bridges
Curved bridges under vertical loads.

## Slide 17: Types of Supports
Pin
Roller
Fixed Support
R(H)
R(V)
R(V)
R(V)
R(H)
M
Notes: Bearings fixed (pinned)
Bearings free (roller
Fixed (integral abutment)
These change the effects within the girder. Are they functioning as intending/designed?

## Slide 18: Span Classification
Simple Span

## Slide 19: Shear
20 kN
5
15
A
B
15 kN
15 kN
A
5 kN
5 kN
B
RA = 20x15/20 = 15 kN
RB = 20x5/20 = 5 kN
20 kN
RA = 20x15/20 = 15 kN
RA = 20x15/20 = 15 kN
A
A
B
B
Notes: 20m long beam with 20 kN load applied
Do example on whiteboard (Nolan to write on Paper)
Ra is going to be bigger than Rb
Sum moments at A
Sum forces in y direction
This would be different if we had a “fixed” end. Could not solve with only “statics”.

## Slide 20: Shear Diagram
20 kN
15 kN
5 kN
15 kN
20 kN
5 kN
Notes: What’s the shear at each location in the beam for this position of load?
Where is it high/low?
It’s high all the way from the load to the support.
High negative or positive
For concrete, that’s where I want more stirrups and would be looking for shear cracks.

## Slide 21: Bending Moment
20 kN
5
15
20 kN
15 kN
5 kN
15 kN
15 kN
15 kN
15 kN
a
15a kNm
Notes: Internal force effects

## Slide 22: Bending Moment Design
20 kN
15 kN
5 kN
15 kN
20 kN
5 kN
5
15
15x5 =
75 kNm
5x15 = 75 kNm
75 kNm
Notes: Where is moment high? It gets lower toward the supports. (for simple spans)
That’s where I want longitudinal reinforcing and bigger steel flanges.
That’s where I’m looking for flexural cracks

## Slide 23: Span Classification
Continuous Span
Deflection
Shear
Moment
Notes: Shear how shear flips at supports but magnitude is still high on both sides.

## Slide 24: Span Classification
Cantilever
Deflection
Shear
Moment
Notes: Eiffel tower

## Slide 25: Stress in Steel
SHORTEN
LENGTHEN
TENSION
COMPRESSION
YIELD STRESS
YIELD STRESS
Notes: Good in both tension and compression
Deforms after yielding without failure

## Slide 26: Steel Bridge Members
ROLLED BEAM
ROLLED BEAM WITH
COVER PLATES
WELDED PLATE GIRDER
RIVETED PLATE GIRDER
BOX GIRDER

## Slide 27: Steel Beams – Bending Stress
WELDED PLATE GIRDER WITH VARYING FLANGE SIZES
ROLLED BEAM
ROLLED BEAM WITH COVER PLATES
Notes: Flanges carry moment
Bigger flanges in areas of large moments, positive or negative.
With rolled beams this is done with cover plates.
Nowadays we use plate girders with varying plate sizes

## Slide 28: Steel Beams – Compression Stress
COMPRESSION FLANGE
CROSS BRACING
Notes: Brace the compression flange.
Concrete deck. Wet concrete

## Slide 29: Steel Beams – Shear Stress
LONGITUDINAL STIFFENERS
BEARING STIFFENERS
INTERMEDIATE
STIFFENERS
Notes: Webs carry shear
Intermediate stiffners for shear resistance. Buckling of web panels
Longitduinal stiffeners due to moment (compression). Piers midspan
Bearing stiffener for web crippling.

## Slide 30: Composite Beam
CONCRETE DECK
STEEL BEAM
SHEAR STUDS
Notes: Increased capacity
Also load sharing
Also required for transvers design of deck

## Slide 31: Stress in Concrete
SHORTEN
LENGTHEN
TENSION
COMPRESSION
STRESS
Notes: Good in compression
Not good in tension
Doesn’t carry load after reaching maximum stress

## Slide 32: Concrete Bridge Members
CONCRETE T-GIRDER
SOLID CONCRETE SLAB

## Slide 33: Concrete Bridge Members
“A” GIRDER
“G” GIRDER
“E” GIRDER
“H”, “HC”, “VH” GIRDER

## Slide 34: Concrete Beams – Bending Stress
TENSION CRACK (Typ)
REINFORCING STEEL

## Slide 35: Concrete Beams – Shear Stress
SHEAR CRACK (Typ)
REINFORCING STEEL
TENSION CRACKS

## Slide 36: Prestressed Concrete
FORMS
Concrete crushes if
prestress too high
Cracks if
prestress too high
May split
Prestressing steel
Prestress Transfer
Tensioning Operation

## Slide 37: Anchorage Stress
b
h
Disturbed Region
Compressive
Tensile
P
fx = P/bh

## Slide 38: Anchorage Stress
0.05
0.10
0.20
0.30
0.34
Bursting Zone
Spalling Zone

## Slide 39: Anchorage Stress
P
Compressive
Tensile

## Slide 40: Anchorage Stress
Concentrated Load
1
2
Possible Tension Cracks

## Slide 41: Prestressed Concrete Bridge Members
SHEAR KEY
SHEAR KEY
BOX GIRDER
(RD, RM, PM)
CHANNEL SHAPED
FC, VF, LF, FM GIRDER
DBT GIRDER
O GIRDER
CAST-IN-PLACE DECK

## Slide 42: Prestressed Concrete Bridge Members
CAST-IN-PLACE DECK
NU GIRDER
PT DUCT
PIER
ENDS OF GIRDERS

## Slide 43: Thermal Stress
INCREASE IN LENGTH
DECREASE IN LENGTH

## Slide 44: Thermal Stress
DECK JOINT
ABUTMENT
ABUTMENT
PIER
EXP. BEARING
EXP. BEARING
FXD. BEARING
Notes: Are these functioning?

## Slide 45: Thermal Stress
DECK JOINT
ABUTMENT
ABUTMENT
PIER
BEARING
BEARING

## Slide 46: Stress in Concrete
BRIDGE DECK
APPROACH
SLAB
APPROACH
SLAB
CONTROL
JOINT
CONTROL
JOINT

## Slide 47: Questions?