## Slide 1: MAJOR BRIDGE INSPECTION FORMS

## Slide 2: Inspection Form Types
Each form has a unique identification or form ID
9 different inspection report forms for bridges with a single span type
1 report for sign bridges
Custom forms can be generated to suit the number & type of spans

## Slide 3: Standard Bridge Inspection Form
Form ID | Span Description | Span Types
TT | Timber Bridges | TT, UT, UX
PCS | Standard Precast Bridges | HH, GC, VH, PG, GR, PE, PPS, VS, SM, SMC, SC, SCC
CUL1 | Single Culvert | RS, SP, FP, MP, WP, TP, CP, BP, AP, XP, RPA, RPO, RPP, RPE, MPL
CULM | Multiple Culverts | Same as CUL1 in any combination
CULE | Culvert extended with a different material or size | RPX, APX, CPX, MPX

## Slide 4: Major Bridge Inspection Forms
Form ID | Span Description | Span Types
TH | Trough Truss Bridges | TH
PT | Pony Truss Bridges | PT
DT | Deck Truss Bridges | DT
SG | Steel Girder Bridges | RB, RG, WG, FR
PSR | Regular Prestressed Girder Bridges | RD, FC, VF, PM, VM, PB, DBT, PQ, PO, LF, FM, RM, PJ
CON | All Cast-In-Place Concreate Concrete Tee Girders Bridges Concrete Flat Slab Bridges | CA, CB, CF, CV, CX, CC CT CS
SS | Other Trusses and Arches | SS
SIGN | Sign Structures | Z

## Slide 5: Common Major Bridge Form Sections
Bridge Site Inventory
Bridge Inspection Details
  Name, Date, Arrive/Depart times
Approach Road
Posting Information
  Vertical clearance
  Posted loading
  Utilities
Structural Condition Rating
Sufficiency Rating
Special Comments for Next Inspection
ERY
Next Inspection Date and Inspection Cycle

## Slide 6: Common Major Bridge Form Sections
Channel
Grade Separation
Structural Condition Rating
Sufficiency Rating
Special Comments for Next Inspection
ERY
Next Inspection Date and Inspection Cycle

## Slide 7: Unique Major Bridge Form Sections
Superstructure
Substructure
Maintenance Recommendations

## Slide 8: Superstructure Section
Common Elements
  Special Features
  Deck Rideability
  Bridge Rail
  Sidewalk
  Span Alignment Problems
  General Rating

## Slide 9: Wearing Surface
SG, DT, CON,
and SS forms
PT, and TH forms
PSR forms

## Slide 10: Deck Top
PT, TH and SS have no Deck Top Element
SG, DT, PSR and CON forms only

## Slide 11: Deck Joints
SG, DT, PSR and SS forms
PT, TH and CON forms

## Slide 12: Deck Drainage
Curbs/ Medians / Wheel / Guards
SG, DT, PSR, CON and SS forms only
SG, DT, PSR, CON and SS forms
PT and TH forms
PT, TH form - No Drainage Element

## Slide 13: Truss Members
Pony and Through Trusses (PT & TH)
TH only
TH only
TH only

## Slide 14: Deck Truss, Other Trusses & Arches (SS)

## Slide 15: Girders/ Beams
PSR only
SG only
CON and SS

## Slide 16: Diaphragm / Cross Frames
Paint
SG, DT, PT, TH, SS others none
SG, DT, PSR, CON, SS none on PT, TH

## Slide 17: Bearings
Not on PT and TH

## Slide 18: Deck Underside
SG, PSR, and CON forms
DT and SS forms
PT and TH forms

## Slide 19: Substructure - Abutments
PT, TH and SS only
PT, TH and SS only
PT and TH only

## Slide 20: Substructure - Piers
PT, TH and SS only
PT, TH and SS only
Not on CON
Not on CON

## Slide 21: Form Review
Inventory items
  Shaded fields on form (TIMS)
  Verify/revise data on form
Element Ratings
  fill all blank fields
  use N or X if necessary
Data on LH Side of Form or Explanation of Condition
  Verify & check off if visible
  Carry over if not visible

## Slide 22: Reason for Inspection
Safety
Maintenance
Management
Condition
Functionality
Rating Considerations

## Slide 23: Maintenance Recommendations (Table 11.1)
Not on PSR

## Slide 24: Maintenance Priority
Rating | Maintenance Priority
5 | No maintenance required
4 | Low priority Recommended is not required If made – not likely before next inspection
3 | Medium priority Before next inspection (6 mo. To 3 years)
2 | High priority Monitor until work is done (within 6 months)
1 | Immediate action

## Slide 25: Road Classification
Indicates current desirable standard (Refer to Table 4.2)
Current Departmental standards are:
Highway Type | Road Classification
Local Roads (graveled) | RUL 207G-60 RUL 208G-60 RUL 208G-90 RUL 209G-90 RUL 210G-90 RUL 210G-100
Local Roads (Paved) | RUL 208-100 RUL 208-110
Secondary Highways | RCU 208-110 RCU 209-110 RCU 210-110

## Slide 26: Road Classification (cont’d)
Indicates current desirable standard (Refer to Table 4.2)
Current Departmental standards are:
Highway Type | Road Classification
Primary Highways (undivided) | RAU 209-110 RAU 210-110 RAU 211.8-110 RAU 213.4-110 RAU 213.4-120
Primary Highways (divided) | RAD 412.4-120 RFD 412.4-130 RAD 616.6-130 RFD 616.6-130 RFD 820.8-110 RFD-1024.5-110

## Slide 27: Major Bridges – Concrete (Table 11.3)
Type | Low | Ave | high
Prestressed Girder** | 45 | 55* | 70*
Precast Girder** | 30 | 35 | 50
Cast-in-Place** | 40 | 50 | 60
Use maximum of 50 years for timber sub-structure
Add 5 years if overlaid with concrete
Add 5 years if strengthened or laterally stressed
Life Expectancy

## Slide 28: Major Bridges – Steel (Table 11.3)
Type | Low | Ave | High
Ridge Frame | 60 | 70 | 80
Welded Girder | 60 | 70 | 80
Deck Truss | 60 | 70 | 80
Rolled Beams | 50 | 60* | 80*
Riveted Plate Girder | 40 | 50 | 70*
Through Truss | 40 | 50 | 70*
Pony Truss | 40 | 50 | 70*
Bailey and Other Types | 30 | 40 | 50
Life Expectancy
Use maximum of 50 years for timber substructure

## Slide 29: Estimated Remaining Life
Major Bridges
Considerations
  Traffic characteristics
    volume, amount of truck traffic, log haul
  Salt usage
    road surfacing, traffic, climatic conditions
  Deck drainage, leakage
  Decay favorable conditions
  Design or rated load capacity

## Slide 30: Questions?