## Slide 1: PREPARATION FOR INSPECTION AND INSPECTION SAFETY

## Slide 2: Inspection Safety
Occupational Health & Safety Act
  high rigging
  scaffold & swing stages
  crane safety and rigging
  confined spaces
  working over water
  working alone

## Slide 3
General Safety Issues
  use proper equipment
  park in a safe location
  avoid unnecessary risk
  assume all electrical is live
  do not wear chest waders in fast moving water
  use caution on ice
  do not enter confined spaces
  un-even ground
  slippery culverts
  fast flowing water
  3-point contact on bridgerails
  inspect facing traffic – be alert
  Working alone. Use the check-in procedure – test it!!
Inspection Safety (Continued)

## Slide 4: Inspection Safety (Continued)
Traffic Safety
  If possible, schedule during low-traffic flow
  Inform road authority
  Park vehicles in a safe location completely off the driving surface
    If not possible due to snow, steep side slopes etc. than vehicle must be parked a minimum of 1.0 m from the outside edge of the shoulder.
    If no safe parking is available, may have to find nearest driveway or field access and walk back to site.
    Avoid parking in vicinity of blind corners or hills
  Inspection vehicles must be equipped with a Cl. 1 or 2 amber LED light bar that remains for the duration of the inspection
  A magnetic sign (24 x 15”) or similar must be on the back of the inspector's vehicle stating “”Bridge/Culvert Inspection in Process” at all times during the Level 1 Inspection.

## Slide 5: Inspection Safety (Continued)
  Wear high visibility vests (must be CSA Cl. 2 standard)
  Be efficient and follow a routine – don’t cross back and forth in traffic un-necessarily
  Be alert – be safe. Always be aware of surroundings, particularly when working near an active roadway
  During Level 1.5 and Level 2 inspections over railways or navigated water obtain permission from Railway/Transport Canada. Ensure all their requirements are met if inspector or equipment is within their ROW

## Slide 6
Personal Equipment
  hard hat (as required)
  proper footwear (non-slip soles)
  hip waders
  chest waders*
  eye protection
  warm clothing
  extra clothing
  rain gear
  1st aid kit
  bug spray
  bear spray
  snake bite kit
  safety harness – Level 2
  life jackets – Level 2
  cell phone, gps
  satellite communication device when working remotely
Personal Safety

## Slide 7
BIM Manual
Reference Manual
Clip board and extra pencils
Camera
Long tape & steel weight
Short (5-8m) wide blade tape
Chipping hammer
Prism pole or similar sturdy device for probing
Pocket knife
Binoculars
Crack width gauge
Angle finder
Flashlight and headlamp c/w extra batteries
Marking crayons
Inspection mirror
Compass
Basic Tools for Inspection

## Slide 8: Basic Tools for Inspection
Surveyor hand level
Regular hand level
Wire brush/scraper
Plumb bob
String line
Measuring pole or laser measuring device
Personal equipment
Shovel
Decontamination supplies (discussed further with Whirling Disease)

## Slide 9
Level 2
portable ladders
  base 1/4 of length from wall
  do not work on top two rungs
  base firm and non-slip
  extension ladders proper overlap
scaffold
  anchor properly
  design = 4X load
  inspect daily
safety harness – Level 2
  adjust to fit
  attach to fixed anchor
  check prior to use
  must be certified for use
Inspection Equipment

## Slide 10
BIM Inspection Forms
  order from BIS
  carry blank forms
  review previous inspections
Bridge File Maps or AT Maps
  shows bridge locations
  GPS co-ordinates
  plan route
  set-up designated check-in person or system – test it!
Bridge Inventory Information
  use to confirm bridge characteristics
  Inspection requirements
  check bridge file number
  update inventory during inspection
Hazard Assessment
  Complete a Field Level Risk Assessment prior to start of inspections.
  A FLRA can represent multiple sites if hazards are similar
Preparation for Inspection

## Slide 11: Whirling Disease
Whirling disease is caused by a microscopic parasite of salmonid fish.
This disease is not harmful to humans or other mammals but can have significant effects on some fish populations. It can be transmitted from infected locations to other water bodies:
  through equipment used for swimming, paddling, boating, water pumping, and fishing
  The movement of fish, mud, and water can potentially spread whirling disease.
Basic Preventative Practices as outlined by Alberta Environment and Parks (AEP)
  Clean
  Drain
  Dry

## Slide 12: Whirling Disease – 2020 Heat Map

## Slide 13: Whirling Disease – 2020 Heat Map

## Slide 14
Decontamination Protocols as they apply to Bridge Inspection:
Different levels of decontamination required depending on what zone you are working in.
AEP has four useful documents on their website that inspectors are required to familiarize themselves with and adhere to:
Decontamination Protocol - Watercraft & Equipment
Decontamination Risk Map
Decontamination Quick Reference Guide
Decontamination Equipment List
  https://www.alberta.ca/whirling-disease.aspx
Whirling Disease

## Slide 15: Whirling Disease
Zone (HUC6 boundary) is identified on BIM form in “Department Comments” area.
Make appropriate preparations prior to inspections.
Development of internal protocols is a requirement.

## Slide 16: Field Groups
Instructors
Randy Bredo
Greg, Roy, Shiva, Rylan, Rahul, Ali
BF 174, BF 225, BF 7859, BF 13044
Calvin Roberts
Steve, John, Teran, Ed, Mitchell, Mackenzie
BF 7859, BF 13044, BF 174, BF 225
Garry Roberts
Mohammed, Jasmine, Ben, Nina, Dan, Rex
BF 13044, BF 7859, BF 225, BF 174

## Slide 17: Questions?