## Slide 1: CULVERTS – BASIC STRUCTURAL CONSIDERATIONS
https://m.youtube.com/watch?v=NTbhyHNA1Vc

## Slide 2: Introduction
Currently there are approx. 8515 bridge size culverts in Alberta which accounts for ~63% of all bridge structures in the province.
Two types of culverts:
1) Flexible Structures (corrugated steel) (~96%)
2) Rigid Structures (concrete, steel or timber)

## Slide 3: Standard Drawings S-1418-20

## Slide 4: Rigid Structures
Concrete (~4%) – either box or pipe
Timber (0.1%) - no longer being built
Smooth wall steel pipe liners (rigid pipe)
No noticeable deflection under loads
Concrete is a durable material
Concrete is relatively expensive

## Slide 5: Rigid Structures

## Slide 6: Flexible Structures
Metal culverts comprise approximately 96% of culvert inventory
Fabricate to almost any shape
Relatively cheap
Proper Backfill & Installation is CRITICAL
Susceptible to structural problems
Prone to corrosion, abrasion

## Slide 7: Flexible Structures

## Slide 14: CSP (field jointing)

## Slide 15: Flexible Culverts
Two Types:
Corrugated Steel Pipe (CSP)
Structural Plate Corrugated Steel Pipe (SPCSP)

## Slide 16: Corrugated Steel Pipe (CSP)
Complete rings fabricated in plant
Rolled helical sections, re-rolled ends
Joined by couplers
Bridge sizes range from 1500 to 3600
Common sizes 1800 to 3000 (in 200mm increments)
Segment produced in lengths to suit transport (2.5 to 15.0 m)

## Slide 17: CSP Properties
Common Thickness
  2.8mm, 3.5mm, 4.2mm
Common Profiles
  68mm (Pitch) x 13mm (depth)
  76mm X 25mm, and 125mm X 26mm

## Slide 18: Structural Plate Corrugated Steel Pipe (SPCSP)
Flat plate is corrugated & punched
Hot dip galvanized then curved to shape
Five thickness – 3, 4, 5, 6, and 7mm
Profiles - pitch x depth
  152 x 51 mm
  380 x 140 mm
  400 x 150 mm
Individual plates are bolted together

## Slide 19: SPCSP (cont.)
Plate lengths
    3,050mm (10 ft)
    3,670mm (12 ft)
Plate width 5N, 6N, and 9N
    N is the circumferential bolt spacing
    N = 3pi (244 mm or 9.6”)
    Ex: Number of bolts in a 3.048m or 10’ diameter ring
    = π x 3048 mm / 244 mm = 39.2 = 39 spaces or 40 bolts per ring

## Slide 20: SPCSP - some recent products
Atlantic Industry's ‘Bolt-a-Plate
    width 1067, length 3N to 16N
Twister Pipe’s ‘MP 200’
    pitch 200, depth 55mm
SuperCor, and Bridge Plate
    (pitch 380, depth 140)
New coating systems

## Slide 21: SPCSP - some recent products
New coating systems
Notes: Black polymer coating for use in areas with corrosive soil.

## Slide 22: SPCSP (field bolting)
Longitudinal Seam Stagger (1N)

## Slide 23: SPCSP Barrel

## Slide 24: SPCSP (longitudinal lapping)

## Slide 25: Properly Lapped Seam Bolt in valley is nearest visible edge

## Slide 26: Improperly Lapped Seam Bolt in valley is farthest from visible edge

## Slide 27: Improperly Lapped Seam Bolt in valley is farthest from visible edge

## Slide 28: SPCSP (seam strength tests)
Both types of laps can carry about the same load
Correctly lapped seams are more ductile – do not typically develop cracks

## Slide 29: Bridge Construction Inspection Manual
https://open.alberta.ca/publications/bridge-construction-inspection-manual-edition-3

## Slide 30: Questions?