## Slide 1: Tender Packages (Consistency with Current Design Bulletins)
Basic Knowledge for Roadway and Bridge Projects Seminar for CEA Members
Edmonton
February 12, 2014

## Slide 2: Design Bulletin 18 Rumble Strip Placement Practices April, 2012

## Slide 3: Rumble Strips …
… are a preventative measure

## Slide 4: Rumble Strips …
… are a preventative measure
… reduce cross-the-centre incidents

## Slide 5: Rumble Strips …
… are a preventative measure
… reduce cross-the-centre incidents
… reduce run-off-road incidents*
* 40% of rural injury crashes are
run-off-road type.

## Slide 6: Why Use Rumble Strips?
Rumble Strips are considered to be the most cost-effective safety measure that has not been universally adopted to date.
Can reduce fatigue-related crashes by between 20% and 80% (according to published studies).

## Slide 7: Shoulder Rumble Strips
On two-lane highways
- shoulders are 1.4 m wide or greater.

## Slide 8: Shoulder Rumble Strips
On two-lane highways
- shoulders are 1.4 m wide or greater.
On multilane (divided) highways
- right shoulder is 1.4 m wide or greater.

## Slide 9: Shoulder Rumble Strips
On two-lane highways
- shoulders are 1.4 m wide or greater.
On multilane (divided) highways
- right shoulder is 1.4 m wide or greater.
- left shoulder (median) is 0.6 m wide or greater.

## Slide 10: Centreline Rumble Strips
- warranted on all undivided paved highways

## Slide 11: Transverse Rumble Strips
On the stop-controlled approaches
of all stop-controlled intersections

## Slide 12: Transverse Rumble Strips
On the stop-controlled approaches
of all stop-controlled intersections
- in rural areas;

## Slide 13: Transverse Rumble Strips
On the stop-controlled approaches
of all stop-controlled intersections
- in rural areas;
- where the posted speed limit is 80 km/h or greater;

## Slide 14: Transverse Rumble Strips
On the stop-controlled approaches
of all stop-controlled intersections
- in rural areas;
- where the posted speed limit is 80 km/h or greater;
- highway and intersecting approaches are paved;

## Slide 15: Transverse Rumble Strips
On the stop-controlled approaches
of all stop-controlled intersections
- in rural areas;
- where the posted speed limit is 80 km/h or greater;
- highway and intersecting approaches are paved;
- not less than 300 m of a residence.

## Slide 17: Rumble Strips shown on standard cross-sections.

## Slide 18: Design Bulletin 75 High Tension Cable Barrier System - Median and Roadside Installation April, 2012

## Slide 19: High Tension Cable Barrier Systems

## Slide 20: Where do serious collisions occur?
60% of fatal crashes involve one vehicle (USA)
70% of single vehicle fatal crashes are Run-off-Road – fixed object or overturn.
Alberta data is similar – about half of fatal collisions occur on roadside.

## Slide 21: 3 Types of Longitudinal Barriers
Rigid:
  Concrete

## Slide 22: 3 Types of Longitudinal Barriers
Rigid:
  Concrete
Semi-Rigid:
  Strong posts of steel, wood or plastic
  Steel beams

## Slide 23: 3 Types of Longitudinal Barriers
Rigid:
  Concrete
Semi-Rigid:
  Strong posts of steel, wood or plastic
  Steel beams
Flexible Barriers:
  High Tension Cable
  Low Tension Cable
  Weak Post Steel Beam

## Slide 24: High Tension Cable Barrier
All types of median barriers can prevent crossover collisions on divided highways.
HTCB is the most forgiving and least costly.

## Slide 25: Traffic Barrier System Selection
Designers are encouraged to
select the most forgiving barrier system
that will provide the required level of protection for the given circumstances and constraints.

## Slide 26: Design Bulletin 68 Roundabout Design Guidelines on Provincial Highways February, 2011 (new draft currently being produced)

## Slide 27: Safety effects of Roundabouts.
Collision rate reduction 39%
Notes: Our degree of confidence in using these figures is high due to multiple sources. The collision reporting rules (especially for pdo’s) varies around the world which accounts for some differences in the predicted impacts. Also, the familiarity of the driving public with roundabouts can relate to performance.

## Slide 28: Safety effects of Roundabouts.
Collision rate reduction 39%
Fatal collision reduction 90%
Notes: Our degree of confidence in using these figures is high due to multiple sources. The collision reporting rules (especially for pdo’s) varies around the world which accounts for some differences in the predicted impacts. Also, the familiarity of the driving public with roundabouts can relate to performance.

## Slide 29: Safety effects of Roundabouts.
Collision rate reduction 39%
Fatal collision reduction 90%
Injury collision reduction 76%
Notes: Our degree of confidence in using these figures is high due to multiple sources. The collision reporting rules (especially for pdo’s) varies around the world which accounts for some differences in the predicted impacts. Also, the familiarity of the driving public with roundabouts can relate to performance.

## Slide 30: Safety effects of Roundabouts.
Collision rate reduction 39%
Fatal collision reduction 90%
Injury collision reduction 76%
Pedestrian Crash reduction 73%
Source: Transport Canada, Clearinghouse for CMFs, Desktop Reference for CRF (FHWA), NCHRP 617 (TRB).
Notes: Our degree of confidence in using these figures is high due to multiple sources. The collision reporting rules (especially for pdo’s) varies around the world which accounts for some differences in the predicted impacts. Also, the familiarity of the driving public with roundabouts can relate to performance.

## Slide 31: Roundabout Policy
Roundabouts shall be considered as the first option
for intersection designs where
a greater degree of traffic control than
a two-way stop is required on a paved roadway.
e.g. signalization or 4-way stop control.
Notes: Our degree of confidence in using these figures is high due to multiple sources. The collision reporting rules (especially for pdo’s) varies around the world which accounts for some differences in the predicted impacts. Also, the familiarity of the driving public with roundabouts can relate to performance.

## Slide 32: Partial Dumbbell
King St Interchange, Fort McMurray, AB

## Slide 33: Single Lane, Major Highway
Hwy 55 & 892, near Cold Lake, AB

## Slide 34: Urban Fringe
Highway 11A & 20, Sylvan Lake, AB

## Slide 35: Urban Highway
Highway 774 & Main Street
Peace River, AB

## Slide 36: Design Bulletins contain updates to standards or practices after consultation / approval has been obtained currently have produced over 75 bulletins If bulletins are not followed, there should be a design exception or some documentation to show rationale / approval for the choice.

## Slide 37: Some jobs have been tendered that do not comply with the current standards. Examples are: Omission of rumble strips (centreline and / or shoulder) Use of conventional barrier instead of HTCB Implications on safety and operating costs

## Slide 38: Possible Remedies: - knowledge of design bulletins (up-to-date); - note in Terms of Reference to follow bulletins; - Region to check the tender package prior to submission; - projects being returned from shelf should consider design bulletin content; - consultants double-check estimates (two signatures).

## Slide 39: Red Flags Bid items that are included: - W-beam guardrail; - Thrie Beam; - Concrete Barrier. - Signals. Bid items that are not included: - Rumble Strip items are zero.